## Slide 1: Harnessing Frequency Diversity in Wi-Fi Networks
Apurv Bhartia
Yi-Chao Chen
Swati Rallapalli
Lili Qiu
MobiCom 2011, Las Vegas, NV
The University of Texas at Austin

## Slide 2: Existing Wi-Fi Protocols
Entire channel as a uniform unit
All symbols are equal
Significant frequency diversity exists
Not all symbols are equal
Header vs. payload symbols
Data symbols vs. FEC symbols (Systematic FEC)
Subject vs. Background symbols

## Slide 3: SNR in a 20MHz Channel
  Frequency selective fading, narrow-band interference
Chart: 
| 1 | 10 | 20 | 30
SNR | 22.125 | 22.997 | 23.383 | 23.152 | 22.406 | 21.305 | 19.988 | 18.48 | 16.378 | 14.029 | 13.009 | 14.156 | 15.951 | 17.787 | 18.133 | 19.456 | 20.142 | 20.312 | 20.328 | 20.007 | 20.127 | 19.998 | 20.128 | 20.652 | 20.546 | 21.115 | 21.88 | 21.387 | 20.676 | 19.474
SNR (dB)
Channel Subcarriers

## Slide 4: Wireless is Moving To Wider Channels
802.11n | Up to 40 MHz
802.11ac | Up to 160 MHz
Whitespaces | 100s of MHz
Ultra Wideband | 100s of MHz to GHz
Frequency diversity increases with wider channels!

## Slide 5: Contributions
Analyze the frequency diversity in real Wi-Fi links
Propose approaches to exploit frequency diversity
  Map symbols to subcarriers according to CSI
  Leverage CSI to improve FEC decoding
  Use MAC-layer FEC to maximize throughput
Joint Optimization
  Unifying our three techniques
  Combine with rate adaptation
  Perform simulation and testbed experiments

## Slide 6: Talk Outline
Trace Analysis
Smart Mapping
Improving FEC Decoding
MAC-layer FEC
Unified Approach
Combine with Rate Adaptation
Results
Approach

## Slide 7: Trace Collection
Intel Wi-Fi Link 5300 IEEE a/b/g/n
5 senders, 3 receivers; with 3 antennas each
5GHz channel 36, 20MHz channel width
1000-byte packet size, MCS 0, TX power: 15 dBm
Traces collected on 6th floor of office building

## Slide 8: Frequency Diversity Does Exist…
Fraction of Packets
Degree of frequency diversity varies across links
Fraction of Packets
Static Channel
Mobile Channel
> 8dB difference
> 10dB difference

## Slide 9: Prediction using EWMA
Exponential Weighted Moving Average (EWMA)
  Uses smoothing of the entire time series
Chart: 
| trace 1 | trace 2 | trace 3 | trace 4 | trace 5
α = 0.1 (best for static) | 0.26782 | 0.80499 | 0.34062 | 0.4482 | 0.76402
α = 0.7 (best for mobility) | 0.33112 | 0.97821 | 0.41758 | 0.54537 | 0.92836
Column1
Chart: 
| trace 1 | trace 2 | trace 3 | trace 4
α = 0.1 (best for static) | 1.4268 | 1.2791 | 1.3864 | 1.1877
α = 0.7 (best for mobility) | 0.73765 | 0.79187 | 0.81786 | 0.58519
Column1
Prediction Error
Prediction Error
Static Traces
Mobility Traces
Single value for ‘α’ does not work for both!

## Slide 10: Prediction Using Holt-Winters
Holt-Winters Algorithm
  Decomposes time series into 1) baseline and 2) linear
  Uses EWMA for both
Chart: 
| trace 1 | trace 2 | trace 3 | trace 4 | trace 5
α = 0.1 (best for static) | 0.26782 | 0.80499 | 0.34062 | 0.4482 | 0.76402
α = 0.7 (best for mobility) | 0.33112 | 0.97821 | 0.41758 | 0.54537 | 0.92836
Holt-Winters | 0.27212 | 0.8266 | 0.34882 | 0.46007 | 0.78429
Chart: 
| trace 1 | trace 2 | trace 3 | trace 4
α = 0.1 (best for static) | 1.4268 | 1.2791 | 1.3864 | 1.1877
α = 0.7 (best for mobility) | 0.73765 | 0.79187 | 0.81786 | 0.58519
Holt-Winters | 0.69399 | 0.70917 | 0.69589 | 0.55366
Prediction Error
Prediction Error
Static Traces
Mobility Traces
Holt-Winters prediction works well!

## Slide 11: Talk Outline
Trace Analysis
Smart Mapping
Improving FEC Decoding
MAC-layer FEC
Unified Approach
Combine with Rate Adaptation
Results
Approach

## Slide 12: A Quick OFDM Primer
Transmit data by spreading over multiple subcarriers
  Each subcarrier independently decodes the symbol
Robustness to multipath fading
Used in digital radio, TV broadcast, 802.11 a/g/n, UWB, WiMax, LTE …
20 MHz Channel, 52 subcarriers
PHY layer Data Frame

## Slide 13: Standard Interleaving
Arranges bits in a non-contiguous way
  Improves performance of FEC codes
  Standard 2-step permutation process
Avoid long runs of low reliability bits but assumes
  all subcarriers are equal
  all bits are equal

## Slide 14: Smart Symbol Interleaving (1)
Map important symbols to reliable subcarriers
  Mapping should maximize throughput
Problem
Given a set of subcarriers, determine symbol-subcarrier mapping that maximizes the expected received payload
i.e.
Non-linear utility function
  Optimal solution is challenging
  We develop several heuristics …
correctly received data bits in FEC group

## Slide 15: Smart Symbol Interleaving (2)
Smart Header/Data
Subcarriers ordered by SNR
Data
FEC
Data
FEC
Smart Data
Data
FEC
Header
Payload
Smart Header
Subcarriers sorted by SNR
Header
Payload
Header
Payload
Data
FEC
Header(Data)
Payload(Data)
Header(FEC)
Payload(FEC)

## Slide 16: Smart Symbol Interleaving (3): Iterative Enhancement
Improves performance of heuristic solutions
Calculate utility,
Iterate:
swap K symbols from one FEC group to another
Calculate new utility,
if (
Swap between best and worst FEC groups

## Slide 17: Leveraging CSI for FEC Decoding
Recover partial PHY-layer FEC groups
  Use subcarrier SNR to extract symbols whose SNR > threshold
Increase FEC group recovery
  LDPC decoder assumes uniform BER
  Accurate knowledge of BER across subcarriers increases FEC group recovery in LDPC
  BER estimated using CSI can significantly help LDPC!

## Slide 18: MAC-Layer FEC
Due to frequency diversity, single PHY-layer data rate might not work for all subcarriers
  Per subcarrier modulation and PHY-layer FEC? [FARA]
  May map symbols within a FEC group to same/adjacent subcarriers bursty losses
  Significant signaling and processing overhead
  Not available in commodity hardware
  Benefits of MAC-layer FEC
  Protection based on symbol importance
  More fine-grained than PHY-layer FEC
  Easily deployable on commodity hardware

## Slide 19: Problem and Challenges
Maximize throughput by selectively adding MAC FEC
Challenge: Search space becomes larger!
  How much MAC FEC to add?
  How to split MAC FEC to differentially protect PHY-layer symbols?
  What FEC group size to use at the MAC layer?
MAC-layer FEC
FEC Group
Redundancy Symbols
Data Symbols
PHY-layer Frame

## Slide 20: MAC-layer FEC: Algorithm
PHY-data
d
db
dg
Split PHY-layer symbols into bad () and good ()
Find best that maximizes eff. delivery rate
MAC-FEC
rg
rb
Total # of symbols transmitted (including MAC FEC)
Estimated # of symbols successfully received

## Slide 21: Talk Outline
Trace Analysis
Smart Mapping
Improving FEC Decoding
MAC-layer FEC
Unified Approach
Combine with Rate Adaptation
Results
Approach

## Slide 22: Unified Approach
Perform Smart Mapping
Optimize MAC-layer FEC
Compute based on partial recovery
Update
Record current (

## Slide 23: Unified Approach + Rate Adaptation
Perform Smart Mapping
Optimize MAC-layer FEC
Compute based on partial recovery
Update
Record current (
For each Rate

## Slide 24: Talk Outline
Trace Analysis
Smart Mapping
Improving FEC Decoding
MAC-layer FEC
Unified Approach
Combine with Rate Adaptation
Results
Approach

## Slide 25: Simulation Methodology
Extensive trace-driven simulation
CSI traces collected using Intel Wi-Fi 5300 a/b/g/n
~20,000 packets for both static and mobile traces
Throughput as the performance metric
Evaluate fixed and auto-rate selection mechanism

## Slide 26
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4 | Trace 5
standard | 0.70366 | 0.37447 | 5.8317 | 2.4777 | 4.2723
smart | 2.5537 | 1.9232 | 9.5498 | 8.2181 | 8.1761
Smart Symbol Mapping
Throughput (Mbps)
Smart mapping schemes give 63% to 4.1x increase
Symbol Mapping (Static Traces)

## Slide 27
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4 | Trace 5
standard | 1.0307 | 0.65729 | 7.3769 | 3.3448 | 5.4763
smart | 14.1212 | 8.8389 | 16.5729 | 16.6018 | 16.3932
CSI-based Hints enabled
Throughput (Mbps)
CSI-based hints give 126% to 13x increase!
CSI-based Hints (Static Traces)

## Slide 28: MAC FEC and Joint Optimization
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4 | Trace 5
standard w/o hint w/o MAC FEC | 2.3247 | 0.79522 | 2.3948 | 1.0272 | 1.1281
standard w/o hint w/ MAC FEC | 2.4954 | 1.6304 | 3.0524 | 3.8054 | 2.342
standard w/ hint w/o MAC FEC | 2.8798 | 0.92157 | 3.117 | 1.2869 | 1.5285
standard w/ hint w/ MAC FEC | 3.3006 | 5.979 | 4.209 | 6.0841 | 5.2557
iterative w/ hint w/ MAC FEC | 6.116 | 6.0586 | 6.1643 | 6.1413 | 5.8999
Throughput (Mbps)
MAC FEC improves performance significantly
  Joint Optimization gives 1.6x to 6.6x benefit
7% to 207%
15% to 549%
1.6x to 6.6x

## Slide 29
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4 | Trace 5
standard | 9.3341 | 12.3312 | 9.9603 | 7.7807 | 7.5563
smart | 11.3531 | 14.3706 | 11.494 | 11.0402 | 10.8813
Smart Symbol Mapping
Throughput (Mbps)
Jointly optimized scheme outperforms the standard
Combining with Rate Adaptation

## Slide 30
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4 | Trace 5
standard | 11.1837 | 13.7043 | 11.3723 | 10.1776 | 10.0304
smart | 14.5297 | 16.6268 | 16.4741 | 16.4996 | 15.6735
CSI-based Hints enabled
Throughput (Mbps)
CSI-based hints + Smart iterative benefits significantly
  - 40% to 134% over the default auto-rate scheme
Combining with Rate Adaptation

## Slide 31: Mobile Traces
Throughput (Mbps)
Throughput (Mbps)
Benefits of CSI hints extend under mobile scenarios
  - Smart Iterative gives 68% to 96% benefit
Smart Symbol Mapping
CSI-based Hints enabled
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4
standard | 10.6792 | 13.7468 | 7.291 | 9.4137
smart | 19.1748 | 24.1695 | 13.5185 | 15.052
Chart: 
| Trace 1 | Trace 2 | Trace 3 | Trace 4
standard | 10.1338 | 13.0532 | 6.8931 | 8.9554
smart | 11.0359 | 13.9551 | 7.6037 | 9.6095

## Slide 32: Testbed Methodology
USRP1 based experiments
Low channel width of 800KHz (artifact of USRP1)
  Inject narrowband interference to ‘recreate’ frequency diversity
Vary interference across different runs
Each run consists of 1000 packets, 1000 bytes each
Use the OFDM implementation in GNU Radio 3.2.2
  192 subcarriers in the 2.49 GHz range
  Implement different interleaving schemes and MAC-layer FEC

## Slide 33: Testbed Results (1)
Chart: 
| Run 1 | Run 2 | Run 3 | Run 4 | Run 5
standard | 88.7168 | 76.9032 | 129.1001 | 100.2 | 425.7
smart | 133.8091 | 165.47 | 184.84 | 273.36 | 613.66
Throughput (Kbps)
Symbol Mapping Schemes
Smart mapping out-performs the standard by 42-173%
Benefits of CSI-based hints are also clearly visible

## Slide 34: Testbed Results (2)
Chart: 
| Run 1 | Run 2 | Run 3 | Run 4 | Run 5
w/o MAC FEC | 74 | 80 | 102 | 77 | 80
w/ MAC FEC | 103 | 124 | 226 | 233 | 260
Throughput (Kbps)
MAC-layer FEC
MAC-layer FEC improves performance significantly
  - Standard mapping improves by 1.4x to 3.3x

## Slide 35: Testbed Results (3)
Chart: 
| Run 1 | Run 2 | Run 3 | Run 4 | Run 5
standard | 164 | 372 | 371 | 342 | 211
smart (joint) | 406 | 521 | 540 | 456 | 402
Throughput (Kbps)
Joint Optimization
Combined approach outperforms default by 33-147%

## Slide 36: Related Work
Frequency-aware rate adaptation [Rahul09, Halperin10]
  We propose other techniques like symbol mapping, CSI as hints
Frequency diversity in retransmissions [Li10]
  Our technique applies to any transmissions
Extensively studied [Bicket05, Holland01, Sadeghi02, Wong06, etc.]
  Our work can be complementary to these!
BER-based rate adaptation [Vutukuru09, Chen10]
  Assume SNR is uniform within the frame
Fragment-based CRC [Ganti06][Han10], error estimating codes[Chen10]
PHY-layer hints [Jamieson07], multiple radios [Miu05, Woo07]
  Easily deployable on commodity hardware
Frequency Diversity
Rate Adaptation
Partial Packet Recovery

## Slide 37: Conclusion and Future Work
CSI exhibits strong frequency diversity
Develop complementary techniques to harness such diversity, and then jointly optimize them
Significant performance benefits are possible
CSI is fine-grained and more challenging to predict
  More robust optimization needed to predict
  Prediction holds the key to performance under mobility

## Slide 38: Questions
apurvb@cs.utexas.edu