## Slide 1: I Am the Antenna: Accurate Outdoor AP Location using Smartphones
Zengbin Zhang, Xia Zhou, Weile Zhang*, Yuanyang Zhang
Gang Wang, Ben Y. Zhao, Haitao Zheng
Department of Computer Science,
University of California, Santa Barbara, USA
*School of Electronic and Information Engineering,
Xian Jiaotong University, China

## Slide 2: Ubiquitous Broadband Access
WiFi network is growing rapidly
  Cisco: WiFi traffic will surpass wired IP traffic in 2015
High density
  We need well tuned and managed WiFi networks!

## Slide 3: AP Location: A Critical Function
Better network planning
Finding rogue APs
Neighboring AP

## Slide 4: Conventional AP Location Methods
Simple method, easy to perform
Very time consuming
Signal Map
Distance
RSS Gradient
RSS Gradient
Do we have a better method to quickly and accurately locate the AP?
Fast, very accurate (10˚)
Expensive (hundreds to thousands of dollars)
Directional Antenna
Low measurement overhead
Low accuracy (often error > 45˚)
20%+ Violations

## Slide 5: Insight: The Body Blocking Effect
Can we use this to detect AP location?
  No…Effect is not clear enough
Our observation
User facing the AP
User’s back facing the AP

## Slide 6: Rotation based Measurement
The difference is significant
  User’s body is much larger than the phone
  User is close to the phone
Chart: User Orientation (degree)
13dB
Facing AP
Back facing AP
We can emulate a directional antenna just by
Rotating with Smartphones

## Slide 7: Generality of the Effect
Chart: 

Devices
  Motorola Droid, HTC G1(Android)
  LG Fathom(WM 6.5)
  iPhone4 (iOS)
Protocols
  802.11 b/g
  802.11n (MIMO)
Postures and body shapes of the user
  7 users in our lab
  Different phone orientations
Environments
  Outdoor LOS/Non-LOS
  Different distances to AP
Chart: 
iPhone 4
User Orientation
User Orientation
RSS(dBm)
Back facing AP
Back facing AP
RSS(dBm)

## Slide 8: Outline
Motivation
Accurate AP Location
Evaluation
Conclusion

## Slide 9: User Rotation based AP Location
Borealis’ Design
Accurate
Directional Analysis
Low
Energy Consumption
Walk for x m
Requirements
Chart: User Orientation
AP direction
RSS profile

## Slide 10: Directional Analysis Is Non-Trivial
Min RSS direction?
Using Min RSS direction would cause large errors
Chart: User Orientation (degree)
Chart: Absolute Angular Error (degree)
For 35% cases,
Error > 45˚
user’s back facing AP?
Actual direction
ERROR=40˚

## Slide 11: Our Directional Analysis Model
Signal degradation occurs at a range of directions
Chart: User Orientation
blocking
sector
RSS
Ideal RSS Profile
Around 90˚
RSS could vary inside the sector, so Min RSS is not accurate

## Slide 12: Locating the Blocking Sector
Find the sector with the largest RSS degradation
  Sliding window
  Sin: average RSS inside
  the sliding sector
  Sout: average RSS outside
  the sliding sector
  degradation = Sout - Sin
Sliding Sector
Chart: User Orientation
| 8 | 28 | 48 | 68 | 88 | 108 | 128 | 148 | 168 | 188 | 208 | 228 | 248 | 268 | 288 | 308 | 328 | 348
Empirical | -2.398 | -6.407 | -6.7604 | -7.6203 | -7.9641 | -6.1735 | -4.6986 | -4.2272 | -3.9604 | -0.673 | 3.3312 | 8.4187 | 11.5001 | 11.2095 | 8.2945 | 3.6849 | -0.1607 | -1.9752
Detected direction
Degradation
Chart: User Orientation

## Slide 13: Navigation
How does a user navigate using directional hints?
  Strawman design: periodic
    Refine AP direction every 20m
  However, nothing is perfect
    Temporal/spatial variation
Our adaptive method
  Measurement confidence
    The similarity of measured RSS and ideal RSS profile
  If confidence is high
    Walk further between measurements
Chart: User Orientation
Actual direction
Detected direction

## Slide 14: Implementation
Application layer
  Leveraging WiFi scan to read RSS
    Default scan is very slow
    Scanning all channels each time
OS layer
  Modified WiFi driver
    Scanning the interested channel only
    Accelerate the process: 10 seconds per rotation (10 times faster)
    Save power: WiFi’s energy consumption is 14 times less

## Slide 15: Testing Scenarios
Simple Line of Sight (Simple LOS)
Complex Line of Sight (Complex LOS)
Non Line of Sight (NLOS)

## Slide 16: Accuracy of Directional Analysis
Chart: Simple LOS
Chart: Simple LOS
We compared Borealis to
  Offline Analysis: clustering-based ML method
    Optimized by training set, can be upper bound of directional analysis
  GUIDE: RSS gradient based
  Min RSS: minimum RSS direction based
Chart: NLOS
  Error < 30˚ for 80%+ cases in Simple LOS
  Error < 65˚ for 80%+ cases in NLOS

## Slide 17: Navigation Efficiency
Chart: Navigation Overhead
| Simple LOS | Complex LOS | NLOS
Periodic | 0.48 | 0.74 | 1.34
Adaptive | 0.15 | 0.37 | 1.07
Chart: 
| Simple LOS | Complex LOS | NLOS
Periodic | 0.48 | 0.74 | 1.34
Adaptive | 0.15 | 0.37 | 1.07
Navigation Overhead:
  Defined as the normalized extra distance a user needs to travel
18%
48%
107%
134%
37%
74%
Navigation Overhead
NLOS Examples

## Slide 18: Locating Indoor APs?
Chart: Absolute Angular Error (degree)
Chart: Absolute Angular Error (degree)
Most APs are mounted inside buildings
We mounted the AP on a table in our lab
  Try to locate it outside in Complex LOS/NLOS environment
  Borealis is fully capable of finding Indoor APs

## Slide 19: Conclusion
AP location is an important function
  Very beneficial in AP deployment and management
Borealis: an efficient and accurate solution for WiFi AP location
  Leveraging the body blocking effect on smartphones
  Feasible even in complex environments
Body blocking effect is general
  i.e. works on GNU Radios in 900MHz/1900MHz/5GHz
  Borealis can be applied to locate other types of transmitters

## Slide 20
Thank you!
Questions?