## Slide 1: Enhance & Explore:
CH-1015 Lausanne
adel.aziz@epfl.ch
http://people.epfl.ch/adel.aziz
Adel Aziz
joint work with
Julien Herzen, Ruben Merz, Seva Shneer, and Patrick Thiran
September 21st 2011
LCA
an Adaptive Algorithm to Maximize
the Utility of Wireless Networks

## Slide 2: Problem Statement
Objective
  Maximize given utility function
Challenges vs. related work
  Work on existing MAC
  No network-wide message passing
  Wireless capacity is unknown a priori
1/14
(Max-Weight based [1])
(IFA [2])
(GAP [3])
[1] Proutière et al., CISS, 2008
[2] Gambiroza et al., MobiCom, 2004
[3] Mancuso et al., Infocom, 2010

## Slide 3: Motivation
WLAN Setting
Inter-flow problem
Optimally allocate resources
Multi-Hop Setting
Intra-flow problem
Avoid congestion
2/14
[3] Heusse et al., Infocom, 2003
[3]

## Slide 4: Network Abstraction
Flow = <IP src; IP dst>
  No scaling problem
Architecture of node j
Information to set at node j at time slot n
  Rate allocation vector:
  Information to monitor at GW at time slot n
    Measured throughput:
3/14

## Slide 5: Network Abstraction
Useful information at time slot n
  Measured throughput:
  Capacity region: (unknown a priori)
  Rate allocation vector:
  Last stable allocation:
  Utility function:
  Level set:
4/14
x1
X*
x2

## Slide 6: ‘Enhance & Explore’ in WLAN
Starts from IEEE 802.11 allocation
  Throughput vector: x[0] = ρ[0] {rate allocation}
  Level set of utility μ[0]: L(x[0], μ[0])
  Remember allocation: r[0] = x[0]
Enhance phase: (Find the next targeted level set)
  If (x[n-1] = ρ[n-1] )
    μ[n] = full-size gradient ascent
  Else
    μ[n] = halved-size gradient ascent
Explore phase: (Find the next allocation)
  Pick point ρ[n] randomly
  If (x[n] = ρ[n] )
    Remember new allocation: r[n] = x[n]
    Go to Enhance phase
  Else
    Repeat Explore phase at most N times, then move to Enhance
μ[0]
μ[2]
μ[3]
μ[1]
Truncated Gaussian pdf
μ[4]
Example: N = 2
5/14

## Slide 7: Optimality Theorem
Theorem for E&E
  Utility of never decreases through time
  converges to an allocation of maximal utility
  Converges for any initial rate allocation
Assumptions for the proof
  Fixed capacity region
  Coordinate-convex capacity region
    Much weaker than convexity!
Future work
  Study speed of convergence
6/14

## Slide 8: Complete Solution: E&E + EZ
GW
  E&E decides the per-flow rate allocation
One-hop nodes
  E&E rate-limits one-hop nodes
Multi-hop nodes
  EZ-flow[1] rate-limits multi-hop nodes
7/14
[1] Aziz et al., CoNEXT 2009

## Slide 9: Practical Implementation
Based on Click[1] with MultiflowDispatcher[2]
Creation of 5 new elements
  MFQueue
  MFLeakyBucket
  EEscheduler
  EEadapter
  EZFlow
Evaluation with
  Asus routers
  Ns-3
[2] Schiöberg et al., SyClick, 2009
8/14
[1] Kohler et al., Transactions on Computer Systems, 2000

## Slide 10: Experimental Results in WLAN
Deployment map:
Without E&E:
With E&E:
(proportional fairness)
9/14

## Slide 11
Inter-flow fairness
  Appropriate queuing is needed (Fair Queuing [1])
  … but it is not enough
10/14
[1] Demers et al., Sigcomm’89
Starvation in Mesh Networks

## Slide 12: Practical Results in Mesh Networks
Deployment map:
Without E&E:
With E&E:
(proportional fairness)
11/14
1-hop flow
3-hop flow
1-hop flow
3-hop flow

## Slide 13: Simulation Results in WLAN
Ns-3 simulator
  Re-use of same Click elements
  More controlled environment
  Possible estimation of capacity
  Computation of optimum
12/14

## Slide 14: Future Work
  Include downstream traffic
  Study and improve the speed of convergence
  Analyze new distributions for the Explore phase
  Study the interaction with rate adaptation
13/14

## Slide 15: Conclusion
Wireless networks suffer from
  Intra-flow problem (e.g., congestion)
  Inter-flow problem (e.g., unfairness)
  Time-variability
  Difficulty/impossibility characterizing the capacity region
Need adaptive algorithms to maximize a desired utility
E&E solves the inter-flow problem in WLAN
Combining E&E and EZ-Flow in mesh networks
  Solves both the inter-flow and intra-flow problem
  Avoids network-wide message passing
  Does not modify networking stack
14/14