## Slide 1: Centaur : Locating Devices in an Office Environment
Rajalakshmi Nandakumar
Krishna Kant Chintalapudi
Venkat Padmanabhan
INDIA

## Slide 2
IT
Manual Tracking
Motivation
Enterprises have a plethora of IT assets.
The physical asset tracking and maintenance is vital for an enterprise

## Slide 3
RFID Based Systems
+ RFID systems can track all kinds of devices.
- Requires additional infrastructure.
RFID Antennas

## Slide 4
Can We ?
What if we consider only computing assets in an enterprise ?
Can we track these devices without any additional infrastructure by leveraging the sensing capabilities of these devices?

## Slide 5
Computing Devices in Office Environment
Only Speaker
Speaker and mic
WiFi, Speaker and mic

## Slide 6
Centaur tracks IT assets in an enterprise by leveraging the WiFi and acoustic sensing capabilities of the devices themselves.
Centaur : Locating IT equipment
WiFi-based
Localization
Location Distributions
Acoustic
Ranging
Geometric Constraints
Fusion

## Slide 7
Why
Fusion?

## Slide 8
Related Work : Acoustic Localization
Schemes like Active Bat and Cricket have ultrasound devices in ceilings and host devices.
Use time of flight measurement to localize.
Measurement of time of flight requires time synchronization.
BeepBeep was the first scheme to do acoustic ranging without time synchronization.

## Slide 9
Acoustic Localization: Issues
Requires deployment of special ultrasound devices.
Large number of beacons because acoustic ranging can be done in the order of few meters.

## Slide 10
Related Work : WiFi Localization
Schemes like Radar, Horus constructs RF maps by fingerprinting every location and use it to localize devices.
  Requires huge effort to construct database.
Schemes like EZ that use RF propagation model to localize devices.
  Accuracy is low compared to the above schemes.

## Slide 11
How Well Does WiFi Localization Work?
Error in m
CDF in %
Tail error is high

## Slide 12
How does Centaur solve these problems by fusing WiFi and Acoustic Localization ?

## Slide 13
Coverage in Centaur
Device with speaker and mic
Device with only speaker

## Slide 14
Coverage in Centaur
WiFi-based
localization
Acoustic ranging
Secondary localization
of peripherals.
Devices with only speaker
Devices with speaker and mic.
Devices with WiFi ,speaker and mic.
Distance
Differences

## Slide 15
Accuracy in Centaur
A
B
P(xA | WiFiA)
P(xB | WiFiB)
dAB
P(xA | WiFiA ,WiFiB , dAB)
P(xB | WiFiA ,WiFiB , dAB)

## Slide 16
Challenges
Acoustic ranging in cluttered office environments.
Accommodating speaker-only (“deaf”) devices.
Fusing WiFi and Acoustic Localization using Bayesian Inference.

## Slide 17
BeepBeep : Acoustic Ranging
Laptop A
Laptop B
dAB
A
N
A
A
B
N
B
A
N
A
B
N
B
B
BeepBeep [Sensys 2007]

## Slide 18
Determining the Onset of Acoustic Signal
Send a known signal – correlate at the receiver, find peak
Chirp/PN sequence have excellent auto correlation properties
6m Line of Sight

## Slide 19
Effect of Multipath in Non-Line of Sight
The shortest path will be weaker than reflected paths

## Slide 20
EchoBeep – Acoustic Ranging for NLOS
Time in ms
Correlation
Time in ms
Time in ms
Time in ms

## Slide 21
Performance of EchoBeep

## Slide 22
Challenges
Acoustic ranging in cluttered office environments.
Accommodating speaker-only (“deaf”) devices.
Fusing WiFi and Acoustic Localization using Bayesian Inference.

## Slide 23
Devices like Desktops may have only Speakers.
EchoBeep can be applied only to devices that have both Speaker and Microphone.
Locating Speaker Only Devices
We find Distance Difference between devices and Use them to localize speaker only devices.

## Slide 24
DeafBeep – Measuring Distance Differences
B
C
A
N
A
B
N
B
B
N
A
A
N
B
A
N
A
C
N
B
C
A
B
C

## Slide 25
Performance of DeafBeep
The uncertainty is maximum when distance difference is close to 0

## Slide 26
Challenges
Acoustic ranging in cluttered office environments.
Accommodating speaker-only (“deaf”) devices.
Fusing WiFi and Acoustic Localization using Bayesian Inference.

## Slide 27: Modeling Centaur as a Bayesian Graph
Each measurement is modeled as a Bayesian Sub graph.
All these sub graphs are put together to form a complete Bayesian graph.

## Slide 28
RA
XA
P(RA = rA| XA = xA )
P(XA = xA )
Sub Graph for WiFi Measurement
Node
Evidence Node

## Slide 29
Bayesian Sub Graphs
2ABC
XC
P(2ABC = ABC|
X = xA , XB = xB , XC = xC)
XA
P(XA = xA)
P(XC = xC)
P(XB = xB)
XB
dAB
XB
P(dAB = d| XA = xA , XB = xB)
XA
P(XA = xA )
P(XB = xB )
EchoBeep
DeafBeep

## Slide 30
Putting it all Together
Laptop A
Laptop B
Desktop D
(Anchor)
Desktop C
(Anchor)
Desktop E
XA
XB
dAB
dAC
dBC
XE
2ABC
2ACE
2BCE
2ACD
2BCD
2ABE
RB
RA
Exact inference of a Bayesian graph with loops is NP-Hard
XA
RA
XA
XB
dAB
XA
XB
XE
2ABE

## Slide 31
Approximate Bayesian Inference
Approximate Bayesian Techniques
Loopy Belief Propagation
Sampling techniques like Gibbs Sampling
Maximum Likelihood approach
These well known techniques don’t converge easily for our problem.

## Slide 32: Bayesian inference in Centaur

## Slide 33
Partition the entire graph into loop free sub graphs and perform exact inference on the sub graphs.
Maximize the joint distribution by searching over the narrowed distribution obtained in the 1st step.
Two Step Process

## Slide 34
First Partition The Graph Into Trees
XA
XB
dAC
dBC
XE
2ACE
2BCE
2ACD
2BCD
RB
RA
Remove all evidence that causes loops – G1
XA
XB
XE
2ABE
Now form the complement graph of G1 and again remove all loop causing evidence nodes – G2
XA
XB
2ABC
G3
XA
XB
dAB
G4
XA
XB
dAB
dAC
dBC
XE
2ABC
2ACE
2BCE
2ACD
2BCD
2ABE
RB
RA

## Slide 35
Use Pearl’s Exact Inference In Cascade
XA
XB
dAC
dBC
XE
2ACE
2BCE
2ACD
2BCD
RB
RA
Find exact inference on G1 using Pearl’s algo
XA
XB
XE
2ABE
Use the inference from G1 as prior for G2 and the run Pearl’s algo
XA
XB
2ABC
G3
XA
XB
dAB
G4

## Slide 36
Now Find Maximum Likelihood
Search for the solution that maximizes the exact joint distribution P(X | E)
We sample each variable using the results of the posterior from the previous step for searching
We used a GA but found that in most practical scenarios, since the distributions were very narrow the search converged very quickly

## Slide 37: Performance of Centaur

## Slide 38
Experiment Setup
Experiments were conducted in office building of area 65m X 35m.
Experiments included all type of devices.
Goal :
To evaluate
Coverage of Centaur
Accuracy of Centaur

## Slide 39
Ranging on Non-Anchor Nodes
Error Decreases even with 2 devices.

## Slide 40
Locating Speaker only Devices
40

## Slide 41
Error in m
Locating Speaker only Devices
50 % error is less than 5m.
As number of devices increases, the error decreases.
CDF in %
Error in m

## Slide 42
8m
27m
1
2
3
4
6
7
8
2
3
4
5
7
8
1
2
7
8
True Location
WiFi Only
WiFi + acoustic
5
6
Composite Setup
By combining acoustic measurements with WiFi, the max error decreased from 13m to 3m.

## Slide 43
Summary
EchoBeep : Performs acoustic ranging accurately in cluttered multipath environments.
DeafBeep : Compute the distance differences between devices to localize speaker only devices.
Centaur fuses the above acquired acoustic measurements with the WiFi measurements to track IT assets accurately without any additional infrastructure

## Slide 44
Thank you