## Slide 1: Strata: Layered Coding for Scalable Visual Communication
Wenjun Hu Jingshu Mao Zihui Huang Yiqing Xue
Junfeng She Kaigui Bian Guobin (Jacky) Shen

## Slide 2: You may have seen these…

## Slide 3: Smartphone cameras as “receivers”

## Slide 4: … everywhere

## Slide 5: Existing codes: All or nothing
Camera view
Minimum resolution needed

## Slide 6: Multi-resolution information display

## Slide 7: Diverse camera hardware
Lumia 1020 ~38MP, 30fps
iPhone 4
5MP, 30fps
Nexus 5
8MP, 30fps
iPhone 5s
8MP, 120fps

## Slide 8: Capture distance vs resolution
Capture resolution < display resolution
Undersampling
Not supported by existing codes!

## Slide 9: Our goal
Multi-resolution encoding and decoding
  Analogous to HM and SVC for scalable channel/source coding
Decoding performance scales with receiver capability and channel condition

## Slide 10: In the rest of the talk…
Undersampled channel
Strata design
Strata performance
Focus on spatial, analogous for temporal
  See paper for temporal mixing, code design, and performance results

## Slide 11: Undersampled channel

## Slide 12: Spatial undersampling
Original image
Captured at 28m , enlarged

## Slide 13: Spatial undersampling
In theory, linear mixing of pixel colors
In practice, messier…
  (Auto-)Focus, exposure, contrast
  Noise at block edges
  …

## Slide 14: Color mixing experiment
Patterns of alternating squares

## Slide 15: Color mixing results

## Slide 16: Color mixing results
For the same distance, close to linear color mixing

## Slide 17: Color mixing results
Darker when further away White is better preserved

## Slide 18: Color mixing results
Less grayscale difference
if minimal contrast

## Slide 19: Strata Design

## Slide 20: Toy example
2 layers
  Black overall
  Also small blocks
Small white blocks
are interference

## Slide 21: A simple SNR (like) model
Signal = # of small blocks of the intended color
Noise = # of small blocks of other colors
  Both noise and interference
This actually reflects color mixing weights for monochrome codes

## Slide 22: A simple SNR (like) model
If SNR > 1, the overall block carries at least 1 bit of information
  Its color can be determined
Key: Control noise/interference
  “Reserve” the color of some blocks

## Slide 23: Basic design
2-layer structure, with reserved block
Enhancement layer block
Base layer block
Reserved block
Ensures black majority
Contiguous to mitigate issues in color mixing

## Slide 24: Harnessing additional bits
Bits from reserved block shape
2 bits from 4 different positions

## Slide 25: Example 2-layer code
Base layer block
Enhancement layer block

## Slide 26: Recursively adding layers
Divide each enhancement block further
Follow the same rule otherwise
Enhancement layer (3rd layer) block
Base layer
(2nd layer) block
Reserved block
(In)Dependency between layers:
structural, but not the information encoded

## Slide 27: Harnessing more bits
Adding smaller (third-layer) blocks in the reserved block

## Slide 28: Harnessing more bits
Doubles the
third-layer capacity
Can further add
fourth-layer blocks

## Slide 29: Choice of parameters
Reserved block size
  Efficiency vs accuracy tradeoff
  Need ½ when not knowing input statistics
“Branching factor”
  Control of granularity
  16 offers a good tradeoff
Details in the paper

## Slide 30: Decoding

## Slide 31: Decoding
Divide into blocks
  Start with Layer 1
Determine per-block colors
  11 blacks, 5 whites
Majority gives overall block color (black)

## Slide 32: Decoding
Continue with finer blocks
Stop if can’t divide further

## Slide 33: Strata performance

## Slide 34: Example Strata image
20cm x 20cm on screen, no error correction

## Slide 35: Decoder implementation
Online Android app & Offline version
Strata test display
Multi-level decoded info

## Slide 36: Performance metric
Goal recap:
The amount of information decoded
scales with capture resolution/rate
Metric: decodable bit/layer count

## Slide 37: Performance (spatial)

## Slide 38: Performance (spatial)
Better camera resolution or shorter distance
More decodable information

## Slide 39: Strata vs Single-layer code

## Slide 40: Strata vs Single-layer code

## Slide 41: Strata vs Single-layer code
Strata balances capacity and supported distance

## Slide 42: Other comparison results
Strata vs frequency domain encoding
Strata vs multi-level grayscales
Strata vs group of codes
Details in the paper

## Slide 43: Related work
Temporal barcode design (inter-frame)
  Unsynchronized 4D Barcodes
Spatial barcode design (per-frame layout)
  PixNet, COBRA
Visual tags
Hierarchical coding on LED arrays
Other work on visible light communications
  E.g., Visual MIMO

## Slide 44: Conclusion
Diverse screen/surface-camera channels
  Hardware diversity
  Capture conditions vary
Strata: Layered coding for scalability
  The amount of information decoded scales with diverse channel conditions

## Slide 45: Thank you!
Questions?