## Slide 1: Enfold: Downclocking OFDM in WiFi
Feng Lu, Patrick Ling, Geoffrey M. Voelker, and Alex C. Snoeren
UC San Diego

## Slide 2: WiFi Power Matters
Researchers report active WiFi radio can consume up to 70% of a smartphone’s energy [Rozner et al. MobiSys 2010]
Smartphone activities are network centric
  80-90% data activities over WiFi [Report: Mobidia Tech and Informa 2013]
  But commercial WiFi chipsets have efficient sleep: 700mW (active) to 10mW (sleep)
  [Manweiler et al. MobiSys 2011]

## Slide 3: Can’t Sleep the Day Away
Power saving mode (PSM) on WiFi: move to sleep state when not actively used
Challenges of WiFi energy savings on smartphones
  real-time/chatty apps
  developer may abuse WiFi sleep policy (constantly awake)
Many variants proposed by the research community for better power saving mechanisms and policies

## Slide 4: Downclocking WiFi Communication
  Trade good SNR for energy savings
We proposed SloMo in NSDI 2013
  Downclocked DSSS WiFi transceiver design (1/2 Mbps)
  5x clock rate reduction
  Fully backwards compatible

## Slide 5: When There is Sparsity
Leveraging information sparsity/redundancy in a variety of application scenarios
  WiFi: downclocked packet detection [Zhang et al. MobiCom 2011], SloMo downclocked Tx/Rx [Lu et al. NSDI 2013]
  Outside WiFi: spectrum sensing [Polo et al. ICASSP 2009], GPS synchronization [Hassanieh et al. MobiCom 2012], etc

## Slide 6: OFDM Signaling is Dense
WiFi (802.1a/g/n/ac) is shifting towards OFDM
OFDM signals are extremely dense, and there is no sparsity in the encoding scheme
Open question as whether it is possible to receive and decode OFDM signals with reduced clock rates
Downclocked OFDM?

## Slide 7: Enfold: Downclocked OFDM Receiver
Backwards
Compatible
Standards
Compliant
WiFi Spec
Change
E-MiLi
[MobiCom 2012]
Enfold
SloMo
[NSDI 2013]
APEnfold: standard WiFi OFDM signal
EnfoldAP: downclocked DSSS transmission (from SloMo)

## Slide 8: 10,000 Foot View of OFDM
IFFT
FFT
1
2
3
4
61
62
63
64
Data
Bits
Time Domain
Signal
Decoded
Bits
1
2
3
4
61
62
63
64
D1
D2
D64
R1
R2
R64
sender
receiver

## Slide 9: Nyquist Likes It Fast
Sampling at the correct rate (2f) yields actual signal
Sampling too slowly yields aliases
“High frequency” signal becomes indistinguishable from “low frequency” signal

## Slide 10: Aliasing Viewed on Frequency Domain
Aliasing effect: addition in frequency domain
Multiple frequency domain responses are aliased into a single value
In general, impossible to recover the original data (think about multiple unknowns but less equations)

## Slide 11: Downclocked OFDM Signaling (50%)
Aliasing effect in OFDM  addition of data encoded on subcarriers in a structured manner
frequency domain subcarrier responses
100%: 64 samples
1
16
17
32
33
48
49
64
50%: 32 samples
+
1
2
31
32
2 unknowns 1 equation

## Slide 12: Downclocked OFDM Signaling (25%)
Aliasing effect in OFDM  addition of data encoded on subcarriers
frequency domain subcarrier responses
100% : 64 samples
1
16
17
32
33
48
49
64
25%: 16 samples
+
+
+
1
16
4 unknowns 1 equation
Finite values for the unknowns?
Possible to recover each unknown given one equation!!
x + y = z, x: [1, 3], y: [2, 5]  z: [3, 6, 5, 8]
z = 6  x = 1, y = 5

## Slide 13: Quadrature Amplitude Modulation (QAM)
QAM: encode data bits by changing the amplitude of the two carrier waveforms: Real (I) and Imaginary (Q)
2-QAM: 1 bit
4-QAM: 2 bits
16-QAM: 4 bits
I
Q
actual response

## Slide 14: Harnessing Aliasing Effect (I)
2-QAM per subcarrier  2 possibilities for data coded on subcarrier
50% downclocking (2 unknowns 1 equation): 4 possible values for each frequency response
2-QAM4-QAM
00
01
11
10

## Slide 15: Harnessing Aliasing Effect (II)
25% downclocking (4 unknowns 1 equation): 16 possible values
Aliasing transforms original QAM into a more dense, but still decodable, QAM
16-QAM
100%: n-QAM
50%: n2-QAM
25%: n4-QAM

## Slide 16: WiFi Reception Pipeline
data bits
Timing Synchronization
Frequency Synchronization
Channel Estimation
Phase Compensation
FFT
Bits Decoding
channel samples

## Slide 17: Enfold Implementation
Implemented on Microsoft SORA platform
Standards-compliant design
Evaluated 6 Mbps 2-QAM 802.11a/g frame reception
Downclocked DSSS transmission (SloMo) for ACKs

## Slide 18: Packet Reception Rate vs SNR (100-Bytes)
Baseline: standard WiFi implementation (@100% clock rate) 3 SNRs: 30/25/20dB.
Well below typical SNR (40dB or more) [Pang et al. MobiSys 2009]

## Slide 19: Packet Reception Rate vs SNR (1000-Byes)
Baseline: standard WiFi implementation (@100% clock rate) 3 SNRs: 30/25/20dB.
Well below typical SNR (40dB or more) [Pang et al. MobiSys 2009]

## Slide 20: Apps WiFi Energy Evaluation
Trace based energy evaluation
  power model based on real measurements [Manweiler et al. MobiSys 2011]
  Conservative: max 35% saving
12 popular smartphone apps
  each app > 5 M downloads
Collect ~200s of real WiFi packet traces
video

## Slide 21: Energy Saving with Enfold
Enfold Energy Savings:
Low data-rate apps: 25% to 34%
Bandwidth hungry apps: 10% to 20%

## Slide 22: Conclusion
Downclocked OFDM WiFi reception is both practical and beneficial for smartphones
  up to 34% energy reduction at 25% clock rate
Tradeoff SNR (throughput) for energy savings using lower data rates while remain downclocked
  a great tradeoff for many popular smartphone apps
Policy impact: introduce a downclocked state into existing WiFi rate selection and power management framework
Applicable in other domains using OFDM

## Slide 23
Thank you!