## Slide 1
  A Practical Traffic Management for Integrated LTE-WiFi Networks
Speaker: Rajesh Mahindra
NEC Labs America
Hari Viswanathan, Karthik Sundaresan, and Mustafa Arslan

## Slide 2: Key Trends
Data traffic exploding on cellular networks
  Rise in video streaming, social networking
Revenue per byte is decreasing
Mobile operators embracing WiFi as a key technology to enhance LTE experience
  Cheap to deploy – unlicensed
  Easy (fast) to deploy – unplanned
  Critical to manage flows across
  APs-Basestations to maximize QoE and resource utilization

## Slide 3: Operator-based WiFi deployments
Absence of network-wide traffic management
  Devices always connect to WiFi when available (static policy)
  Past focus has been authentication methods over WiFi

## Slide 4: Today: Devices always connect to WiFi

## Slide 5: Operator-based WiFi deployments
Absence of network-wide traffic management
  Devices always connect to WiFi when available (static policy)
  Past focus has been authentication methods over WiFi
Absence of tight data-plane integration
  3GPP based deployments have high CAPEX
    Requires backhauling WiFi traffic through mobile core
    Increased investment in infrastructure

## Slide 6: Today: Resistance to Tight Integration of LTE and WiFi
LTE Core-Network
ePDG
3GPP standard WiFi Gateway
PDN-gateway
MME
Serving-gateway
INTERNET
Increased backhaul
costs

## Slide 7: Operator-based WiFi deployments
Absence of network-wide traffic management
  Devices always connect to WiFi when available (static policy)
  Past focus has been authentication methods over WiFi
Absence of tight data-plane integration
  3GPP based deployments have high CAPEX
    Requires backhauling WiFi traffic through mobile core
    Increased investment in infrastructure
  Inability to perform dynamic network selection
Result
  Diminishes the potential effectiveness of WiFi
  Degrades the user Quality of Experience (QoE)

## Slide 8: Opportunity
State of the Art: Client-side solutions
Qualcomm’s CnE, Interdigital SAM
  Static policies (application level) enforced locally on each client
  QoE requirements provided by the application on the client
  Client-side decision making -> inefficient use of network resources
Operator agnostic mobile service (MOTA), in Mobicom 2011
    Requires frequent network state information from each base station
    Incompatible with standards -> difficult to deploy
    Individual decisions by client -> sub-optimal
      Inability for Mobile Operators to perform effective network-wide traffic management!

## Slide 9: Our Idea: A Traffic Management Solution
LTE Core-Network
WiFi Gateway
Traffic Manager
Maps user flows to appropriate network(LTE/WiFi)
Centralized management -> Efficient use of network resources
Reduces backhaul costs -> Facilitates dynamic traffic mgmt
Operates for each LTE cell -> Scalable
Standards agnostic -> Easily Deployable
PDN-gateway
MME
Serving-gateway
Network Interface Assignment
Switching Service

## Slide 10: Components
Network Interface Assignment Algorithm (NIA)
  Goal: Dynamically maps user traffic flows to appropriate LTE basestation or WiFi AP
Interface switching service (ISS)
  Goal: Switch current user flows from WiFi AP to LTE or vice versa based on decisions from NIA

## Slide 11: Component 1: NIA

## Slide 12: Problem Formulation
Consider an LTE cell and multiple WiFi APs in its coverage area
Assign basestation/ AP to each flow
  Maximize sum of users flows’ QoE
QoE captured using “utility”
  Weighted PF provides differential QoE
Pricing function supports 2 models
  Based on data usage
  Based on price/byte
Weight
Throughput
Network Pricing

## Slide 13: Throughput Models
LTE basestation performs weighted PF
WiFi AP performs throughput based fairness
Algorithm does not depend on specific scheduler
  WiFi APs may perform weighted PF

## Slide 14: Problem depiction
3Mbps
5Mbps
1Mbps
2Mbps
4Mbps
8Mbps

## Slide 15: Problem depiction
4Mbps
6Mbps
2Mbps
3Mbps
2Mbps
5Mbps

## Slide 16: Problem depiction
5Mbps
7Mbps
3Mbps
3Mbps
3Mbps
7Mbps

## Slide 17: Network Interface Assignment (NIA)
Problem is NP-Hard
  Including the simplest topology of an LTE cell and a WiFi AP
NIA is a two-step greedy heuristic
  Considers each AP-basestation in isolation
  Fixes assignment for AP that maximized incremental utility
  Iterate till all hotspots are covered
  Complexity is O(K2S2), where K = # clients, S = # APs

## Slide 18: NIA Example
Trigger - arrival/departure of clients or periodic
Step 1: In each WiFi hotspot, partition clients into two sets,
LTE and WiFi, so that sum of utilities is maximized

## Slide 19: NIA Example
Step 2: Finalize interface assignment for clients in the WiFi hotspot with the highest incremental utility

## Slide 20: NIA Example – Iterate
Repeat 1&2 with the new initial condition until all hotspots are covered
Done!

## Slide 21: Component 2: Interface Switching Service

## Slide 22: Design Considerations
Mid-session network switching capability facilitates dynamic traffic mgmt
Leverage HTTP characteristics
  HTTP traffic (esp video and browsing) dominates (>90% of internet)
  Session content(s) are downloaded using multiple HTTP requests
    Video streaming use HTTP-PD (Progressive Download) or DASH (Dynamic Adaptive Streaming over HTTP): A HTTP-GET request/chunk
    Browsing: A HTTP-GET request/object
DASH Server
HTTP
TCP
Multi-resolution
video
VIDEO
VIDEO
VIDEO
Clients
HTTP GET

## Slide 23: Interface Switching Service (ISS)
Switch
Interface
LTE
Interface to NIA
HTTP based
Video streaming/
Browsing
Control
Traffic
WiFi
LTE
HTTP-GET
ISS Controller
Application /
Browser
HTTP Proxy
Control Logic
Mobile Device
Internet
Other types of traffic can leverage existing 3GPP standards for seamless interface switching
Switch to WiFi

## Slide 24: Prototype
Linux Laptop
(Client)
NEC LTE Basestation
WiFi Gateway
Dlink
WiFi AP
OpenEPC
LTE Core
HTTP
requests
Chrome Browser
Shrpx HTTP Proxy
ISS Control
ATOM
NIA Algorithm
Squid HTTP Proxy
Squid HTTP Proxy
ISS Control

## Slide 25: Experiment 1: Large-scale evaluation
Topology: 1 LTE basestation and 3 WiFi APs
Result: ATOM performs better than client-side solutions

## Slide 26: Experiment 2: Benchmarking the ISS
Measured the time taken for flows to switch using ISS:
  HTTP based video streaming flows
  Hulu (uses HTTP-DASH) v/s Youtube(uses HTTP-PD)
Insight: Switching time improves with DASH streaming
  DASH flows use smaller chunk sizes to ensure adaptive-ness to changing network conditions

## Slide 27: Summary
Operators have to look towards exploiting multiple access technologies to increase capacity
  WiFi offers the cheapest alternate to cellular
Our Contributions: a traffic management solution that assigns user flows to LTE basestation/WiFi APs
  Low complexity, scalable algorithm for flow assignment
  Network-based solution more effective than client-side solutions
  HTTP based switching provides dynamic flow assignment at lower costs