## Slide 1: Where Are You From? Confusing Location Distinction Using Virtual Multipath Camouflage
Song Fang, Yao Liu
Wenbo Shen, Haojin Zhu

## Slide 2: Content
Location distinction
Virtual multipath attacks
Defense
Experiment
Summary

## Slide 3: Goal of location distinction
Detect a wireless user’s location change, movement or facilitate location-based authentication.

## Slide 4
Wireless sensor network: Location distinction can prevent an unauthorized person from moving the sensors away from the area of interest
Applications:

## Slide 5: Example 1:

## Slide 6
Example 1 (Cont’d):

## Slide 7: Applications:
Wireless sensor network: Location distinction can prevent an unauthorized person from moving the sensors away from the area of interest
Sybil attack: Location distinction can detect identities originated from the same location

## Slide 8
Example 2:

## Slide 9
X
Example 2 (Cont’d):
From the same location

## Slide 10
Applications:
Wireless sensor network: Location distinction can prevent an unauthorized person from moving the sensors away from the area of interest
Sybil attack: Location distinction can detect identities originated from the same location
RFID: Provide a warning and focus resources on moving objects (Location Distinction [MobiCom’ 07]).
Notes: Besides, RFID tags are widely used for tracking inventory and maintaining the physical security.

## Slide 11
Example 3:
Move
Control
Notes: Location distinction can provide a warning on moving objects and is helpful to allocate resources to be focus on moving objects, like the camera following the moving object as shown in the figure.

## Slide 12
Example 3:
Move
Control

## Slide 13: Existing ways to realize location distinction
Wireless channel characteristics
Change
Location change
Spatial uncorrelation property
Attack: Generate “arbitrary” characteristic
FAIL!!

## Slide 14
Multipath components
  Component response:
  Characterizes the distortion that each path has on the multipath component
Channel impulse response: The superposition of all component responses
Multipath effect
Received signal
Transmitted signal
Notes: And each path performs like a time and space varying filter, and distorts the multipath component.
The effect of such filter can be called as component response. In general, the component response characterizes the distortion that each path has on the multipath component.

## Slide 15
  The channel impulse response changes as the receiver or the transmitter changes location
Channel impulse response
Channel impulse responses can be utilized to provide location distinction.
  Calculate the difference

## Slide 16: Channel Estimation
Training sequence based channel estimation
Training Sequence x
x
y
Estimator
x
h
Training Sequence x
Channel Impulse response

## Slide 17: Channel Estimation (Cont’d)
  Rewrite the received symbols
A Toeplitz matrix
Least-square (LS) estimator

## Slide 18: Content
Location distinction
Defense
Experiment
Summary
Virtual multipath attacks

## Slide 19: Example: Creating a virtual multipath

## Slide 20: Attack Overview: delay-and-sum process.
The ith delayed signal copy
Virtual channel impulse response
The attacker’s aims to make

## Slide 21: Technical Challenge: Obtaining the weights
Send the aggregated signal to the real multipath channel

## Slide 22: Content
Location distinction
Defense
Experiment
Summary
Virtual multipath attacks
Notes: In general, one key cannot open two doors at the same time.

## Slide 23
Defending against the attack: Adding a helper
Notes: Thus, a dramatic change of estimated channel impulse responses at the helper can indicate the potential existence of virtual multipath attacks.

## Slide 24
Defending against the attack: Adding a helper
In this case, the attacker must know the real channel impulse response between herself and the helper.
Notes: Similarly, if the attacker knows the real channel impulse between herself and the receiver’s helper and creates a virtual channel to fool the helper, the channel impulse responses estimated at the receiver side would be inconsistent.

## Slide 25
Defending against the attack: Adding a helper
For Receiver:
For Helper:

## Slide 26
Attackers with helper
Can be set passively: it doesn’t actively send out wireless signals to channel
To fool both the receiver and the receiver’s helper, the attacker needs to know the real channel impulse responses:
Fail to launch attacks
Unknown

## Slide 27: Content
Location distinction
Defense
Experiment
Summary
Virtual multipath attacks
Notes: About the experiment, we performed it outside our lab in USF.

## Slide 28
Experiment floorplan
Transmitter: RX
Receiver: 10 locations
Each node: a USRP connected with a PC
Trials: 100 per location
Multipath: L=5
Notes: The receiver estimated the channel impulse response from the received signals and verifies whether there is a location change by compares a newly estimated channel impulse response with an old one. For each estimates, we perform 100 trails.

## Slide 29: Example attacks I
Randomly chosen channel impulse response
Euclidean distance:

## Slide 30: Example attacks II
Euclidean distance:
Recover another channel impulse response in another building (CRAWDAD data set[1])
[1] SPAN, “Measured channel impulse response data set,” http://span.ece.utah.edu/pmwiki/pmwiki.php?n=Main.MeasuredCIRDataSet.

## Slide 31: Overall attack impact
95%
is much larger than
with high probability
5%
dest = || estimated CIR under attacks - chosen CIR ||
0.25
0.9
dreal = || estimated CIR under attacks - real CIR ||
Notes: This means that dreal is much larger than dest with high probalility, therefore, the attacker can drag the estimated value of channel impulse response far away from its true value and make it very close to her specified one.
With a carefully selected threshold, virtual multipath attacks make the location distinction false alarm rate to be very high. For example, if the threshold is 0.5, when the attack is launched, the receiver will think the transmitter moves because all the differences of the attack and the reference channel exceeds the threshold of 0.5. However, the estimated channel and the real channel are actually measured at the same location. Thus the false alarm rate is raised to 100% under the virtual multipath attack.

## Slide 32
Experiment floorplan
Place the attacker and the helper at each pair of the 10 locations: 10×9=90 pairs.
Attacker
Helper
Notes: Two training sequences are used for estimating the channel impulse responses.
Then, we first show the feasibility of our defense method and then evaluate the performance.

## Slide 33: Defense feasibility evaluation
Receiver
Receiver’s helper (Location 8)
The Euclidean distance between both estimates:
Attacker: Location 2
Notes: The attacker launches the virtual multipath attack. Both the receiver and the helper do the channel estimation from two successive transmissions and then calculate the Euclidean distance between two estimates.
There two figures show the channel impulse responses estimated using training sequences x1 and x2 at the receiver and the helper.
We can see that the distance at the receiver is very small so that it can not detect the virtual multipath attack by itself. However, at the helper, the distance dhelper is much larger so that the helper can effectively help to detect the attack.

## Slide 34: Defense performance evaluation
Conclusion: The helper node is effective to help detect virtual multipath attacks.
Notes: In terms of detection and false positive rates,
The helper may use a threshold to enforce the location. If the d helper is larger than the threshold, the attack is assumed.
The detection rate is the probability that dhelper is larger than the threshold when there is indeed an attack.
The false positive rate is the probability that dhelper is larger than the threshold when there is no attack.

## Slide 35: Content
Location distinction
Defense
Experiment
Summary
Virtual multipath attacks

## Slide 36: Summary
We identified a new attack against existing location distinction approaches that built on the spatial uncorrelation property of wireless channels.
We proposed a detection technique that utilizes a helper receiver to identify the existence of virtual channels.

## Slide 37: Thank you! Any questions?