## Slide 1: Rethinking Energy-Performance Trade-Off in Mobile Web Page Loading
Duc Hoang Bui, Yunxin Liu, Hyosu Kim,
Insik Shin, Feng Zhao

## Slide 2: Motivation
Web browsers: high energy consumption
  Core applications on smartphones
Battery-powered smartphones: limited energy
  Necessary to reduce energy consumption

## Slide 3: Motivation
Web browsers: high energy consumption
  Core applications on smartphones
Battery-powered smartphones: limited energy
  Necessary to reduce energy consumption
User experience: uncompromisable factor
  1-second delay in Bing search engine results in a 2.8% drop in revenue per user [1]
  “As users migrate to mobile, page load time is perhaps the most important metric we have” [2]
[1] O’Reilly Velocity Web Performance and Operations Conference, 2009
[2] Howard Mittman, VP and publisher of Condé Nast, 2015

## Slide 4: Goal
Reduce energy consumption of web page loading without degrading user experience
  No increase in page load time

## Slide 5: Approach
Analyze architectures and behaviors of popular mobile web browsers
  Chromium, Firefox, UC Browser on Android
  Note: Chrome = Chromium + proprietary technologies

## Slide 6: Approach
Analyze architectures and behaviors of popular mobile web browsers
  Chromium, Firefox, UC Browser on Android
  Note: Chrome = Chromium + proprietary technologies
Identify energy inefficiency issues

## Slide 7: Approach
Analyze architectures and behaviors of popular mobile web browsers
  Chromium, Firefox, UC Browser on Android
  Note: Chrome = Chromium + proprietary technologies
Identify energy inefficiency issues
Develop energy saving techniques

## Slide 8: Approach
Analyze architectures and behaviors of popular mobile web browsers
  Chromium, Firefox, UC Browser on Android
  Note: Chrome = Chromium + proprietary technologies
Identify energy inefficiency issues
Develop energy saving techniques
Evaluate on top 100 U.S. websites
  Save significant system energy (e.g., 24% on average) while not increasing page load time

## Slide 9: Energy inefficiency issues
Mobile browsers optimized for performance, not energy
  “Direct port” from desktop versions
  Maximum processing speed regardless of input data
Overhead and redundant computation
Underutilization of heterogeneous architectures
Notes: Identified issues
High energy cost of progressive web resource processing
Unnecessary high painting rate
Underutilization of energy-efficient little cores on big.LITTLE architecture

## Slide 10: Energy inefficiency issues (1/3)
High energy cost of progressive web resource processing
  For each small data, the whole data rendering pipeline executed
  E.g., read system calls return only 1.3 KB data on average from network
Processing
Time
Data
Processing
Processing
Processing
Data
Data
Data

## Slide 11: Energy inefficiency issues (1/3)
High energy cost of progressive web resource processing
  For each small data, the whole data rendering pipeline executed
  E.g., read system calls return only 1.3 KB data on average from network
  High inter-process communication (IPC) overhead
    Multi-process architecture browsers
The Internet
Renderer
Process
Browser
Process
Data and control flow
Process boundary
IO thread
Rending Engine Main thread
Compositor
GPU Thread
Chromium web browser architecture

## Slide 12: Energy inefficiency issues (2/3)
Unnecessary high painting rate
  Visible screen changes can be very small during web page loading
  Painting: from models in memory to pixels on screen
<html>
HTML document
Document Object Model (DOM) tree
Resource
Model
Image
Rendering
Painting
Pixels

## Slide 13: Energy inefficiency issues (2/3)
Unnecessary high painting rate
  Visible screen changes can be very small during web page loading
  Painting: from models in memory to pixels on screen
  E.g. Loading instagram.com, containing no animation
    Average 23-32 frames/s (Chromium, Firefox), fixed 60 fps on UC Browser
    90% of paints generate zero visible changes on screen (in Chromium)
      Off-screen paints
Chart: Screen changes per paint (%) Bin

## Slide 14: Energy inefficiency issues (3/3)
Underutilization of energy-efficient little cores on big.LITTLE architecture
  Current OS scheduler schedules threads based on load instead of quality of service (QoS)
Chart: Frequency (MHz)
| 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300
Little core | 478 | 431 | 399 | 392 | 379 | 389 | 390 | 390 | 392
Big core | 530 | 530 | 534 | 540 | 552 | 554 | 559 | 571 | 606 | 648 | 706 | 777
(a) Energy consumption on Samsung S5 Exynos

## Slide 15: Energy inefficiency issues (3/3)
Underutilization of energy-efficient little cores on big.LITTLE architecture
  Current OS scheduler schedules threads based on load instead of quality of service (QoS)
  E.g. Loading instagram.com
    Chromium: 89% of threads’ time on big cores
    Firefox: 84% of Gecko rendering engine on big cores
Chart: Frequency (MHz)
| 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300
Little core | 478 | 431 | 399 | 392 | 379 | 389 | 390 | 390 | 392
Big core | 530 | 530 | 534 | 540 | 552 | 554 | 559 | 571 | 606 | 648 | 706 | 777
Chart: Web browser threads
| CompositorRasterWorker | CrRendererMain | Compositor | Chrome_ChildIOThread | Chrome_IOThread | AsyncTransferThread | CrBrowserMain | Chrome_InProcGpuThread | Chrome_ChildIOThread/GPU | SimpleCacheWorker | Other
Little cores | 0.14796 | 0.91251 | 0.5937 | 2.0096 | 1.6273 | 0.33358 | 1.743 | 0.97597 | 0.89925 | 1.8186 | 0.2051
Big cores | 21.3852 | 14.0173 | 13.7395 | 10.0384 | 6.909 | 6.8113 | 4.96 | 3.6698 | 3.6415 | 1.7661 | 1.7953
blank | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(a) Energy consumption on Samsung S5 Exynos
(b) Execution time of Chromium threads

## Slide 16: Energy saving techniques
Rethink energy-performance trade-off
  Energy consumption: first-class citizen on smartphones
Reduce redundant computation
  Adjust processing to the user-perceived content changes
Utilize energy efficiency on heterogeneous architectures
Notes: Guidelines for web browsers
  Reduce high cost of incremental resource processing
  Remedy unnecessary high painting rate
  Improve utilization of little cores on big.LITTLE architecture
Energy saving techniques
  Network-aware Resource Processing
  Adaptive Content Painting
  Application-Assisted Scheduling

## Slide 17: Network-aware Resource Processing
Perform batch processing of web resources
  Reduce overhead on small data sizes
Trade-off: energy saving vs. delay
  Large batch size: lower energy but high delay
  Progressive processing: lower delay but high overhead
Processing
Time
Data
Processing
Processing
Processing
Data
Data
Data
Processing
Time
Data
Batch processing
Progressive processing

## Slide 18: Network-aware Resource Processing
Batch size: adaptive to user-perceived content changes
  Download speed: light-weight approximation of user-perceived content changes
  Increase on fast networks to save more energy
  Decrease on slow networks to reduce delay
Batch size determined by a buffer threshold
  : determines the maximum delay for a chunk of data (e.g., 0.5 sec)
: maximum delay time in the buffer
Buffer threshold
Buffer size
Batch size

## Slide 19: Adaptive Content Painting
Aggregate multiple content paints
  Reduce unnecessary computation of small-visible-change paints
Content1
Display1
Time
Content2
Display2
Paint1
Paint2
Time
Content1
Content2
Display2
PaintA
High painting rate
Adaptive painting rate
≈

## Slide 20: Adaptive Content Painting
Aggregate multiple content paints
  Reduce unnecessary computation of small-visible-change paints
Trade-off between user experience (UX) and energy
  Low frame rate: less energy but worse UX
  High frame rate: smoother UX but higher energy consumption

## Slide 21: Adaptive Content Painting
Aggregate multiple content paints
  Reduce unnecessary computation of small-visible-change paints
Trade-off between user experience (UX) and energy
  Low frame rate: less energy but worse UX
  High frame rate: smoother UX but higher energy consumption
paint_rate parameter: maximum content painting rate
  Dynamically adapt to content changing speed
  Light-weight approach
    Increase linearly when content changes fast
    Decrease to a minimum value when content changes slowly

## Slide 22: Application-Assisted Scheduling
Better utilize little cores on big.LITTLE architecture
  Leverage internals of applications for scheduling
  Schedule threads according to QoS
QoS requirement: frame painting time of browser
Little cores
Big cores
High load
Low load
Load-based scheduling
Little cores
Big cores
QoS violated
QoS satisfied
QoS-based scheduling

## Slide 23: Application-Assisted Scheduling
Better utilize little cores on big.LITTLE architecture
  Leverage internals of applications for scheduling
  Schedule threads according to QoS
QoS requirement: frame painting time of browser
Dynamic thread-to-core assignment
  Move threads to big cores: when QoS about to be violated
  Bring threads back to little cores: when QoS satisfied
Little cores
Big cores
High load
Low load
Load-based scheduling
Little cores
Big cores
QoS violated
QoS satisfied
QoS-based scheduling

## Slide 24: Implementation
Prototype based on Chromium version 38 (16 million lines of code)
Buffered resource handler: Network-aware Resource Processing
VSync monitor: Adaptive Content Painting
Thread management module: Application-Assisted Scheduling
The Internet
Resource Handlers
Renderer
Process
Browser
Process
Shared Resource Buffer
Data and control flow
Process boundary
Compositor
Compositor Raster Worker
Command and Texture Buffer
GPU Thread
Async Transfer Thread
IO thread
Resource Dispatcher
Rendering Engine
Javascript Engine
Network Stack
Disk Cache
Child IO Thread
VSync Monitor
Resource Dispatcher Host
Renderer Main
Browser Main
a
Instrumented module

## Slide 25: Evaluation
Experiment setup
  Emulated testbed: repeatable experimentation
  Common 3G network condition
    2 Mbps download, 1 Mbps upload bandwidth, 120 ms RTT
  Web Page Replay tool: record and replay pages
Data set
  Top 100 websites in the U.S. by Alexa.com in May 2014
Devices
  S5-E: Galaxy S5 Exynos (big.LITTLE processor)
  S5-S: Galaxy S5 Snapdragon (symmetric processor)
Metric: Page load time (W3C Navigation Timing specification)
Automation tool
  Two modules: on smartphone and on PC controlling Monsoon power monitor, time synchronized
  Each configuration and website tested at least 5 times

## Slide 26: Video demo: facebook.com
cps.kaist.ac.kr/eBrowser

## Slide 27: Effectiveness of all techniques
Galaxy S5 Exynos (big.LITTLE architecture)
  24.4% system energy saving, including LCD screen
  Page load time decreased by 0.38% (29 ms)
Chart: Average energy saving (%)
 | 1
Chart: Average PLT increase (%)
blank | 0

## Slide 28: Effectiveness of all techniques
Chart: Average energy saving (%)
 | 1
Galaxy S5 Exynos (big.LITTLE architecture)
  24.4% system energy saving, including LCD screen
  Page load time decreased by 0.38% (29 ms)
Galaxy S5 Snapdragon (symmetric processor)
  11.7% system energy saving (without Application-Assisted Scheduling technique)
  Page load time increased by only 0.01% (6.7 ms)
Chart: Average PLT increase (%)
blank | 0

## Slide 29: Effectiveness of each technique
Energy saving
  Application-Assisted Scheduling (AAS): most effective
  Network-aware Resource Processing (NRP) and Adaptive Content Painting (ACP): similar effectiveness
Chart: Average energy saving (%) on S5-E
 | 1

## Slide 30: Effectiveness of each technique
Energy saving
  Application-Assisted Scheduling (AAS): most effective
  Network-aware Resource Processing (NRP) and Adaptive Content Painting (ACP): similar effectiveness
Page load time increase of individual technique is small
  Maximum 0.76% average increase (NRP) on Galaxy S5 Snapdragon
Chart: Average PLT increase (%) on S5-E
 | 1
Chart: Average energy saving (%) on S5-E
 | 1

## Slide 31: User perceived experience
User study: 18 users, compare our vs. default browsers
  Test 1: observe loading speed and smoothness of 10 random websites
  Test 2: do real web browsing for 5 minutes

## Slide 32: User perceived experience
User study: 18 users, compare our vs. default browsers
  Test 1: observe loading speed and smoothness of 10 random websites
  Test 2: do real web browsing for 5 minutes
Results: Minimal difference between our and default browsers
  All users want to use our revised browser
    72% users would always use, 28% users would use when low battery
Chart: 
| Page loading speed | smoothness | Page loading speed | Overall speed | On top 100 sites | In real usage cases
Average | 0.038889 | -0.016667 | -0.11765 | -0.17647
Better
Worse
Same
User experience

## Slide 33: Case study: All techniques
Significant reduction of power consumption
E.g., System power reduction: 5.3 W (Default) vs. 1.4 W (ours)
Chart: Time (sec)
Loading infusionsoft.com

## Slide 34: Case study: AAS technique
Significant increase of utilization of little cores
  E.g., 25% (Default) vs. 60% (Application-Assisted Scheduling)
Chart: Time (sec)
Loading infusionsoft.com
Chart: Time (sec)

## Slide 35: Case study: NRP and ACP techniques
Significant reduction of threads’ execution time
  E.g., Chrome_ChildIO thread execution time reduced by 65% (NRP only)
Chart: Web browser threads
| CompositorRasterWorker | CrRendererMain | Chrome_IOThread | Compositor | CrBrowserMain | AsyncTransferThread | Chrome_ChildIOThread | Chrome_InProcGpuThread | SimpleCacheWorker | Chrome_ChildIOThread/GPU | Other
Default | 8.684 | 6.3838 | 4.575 | 3.5828 | 3.2985 | 2.9352 | 2.4201 | 2.2579 | 2.1266 | 1.0831 | 0.26909
NRP | 1.8312 | 5.505 | 4.5309 | 2.1439 | 2.7132 | 1.8579 | 0.84094 | 1.2891 | 2.2601 | 0.45834 | 0.26531
blank | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 36: Evaluations on other environments and browser
Evaluation | Average system energy saving (%) | Average page load time increase (%)
Fast network (20 Mbps download, 10 Mbps upload, 50 ms RTT) | 21.8 | 0.1
3G network (3G network interface used) | 22.5 | 0.4
Web page loading with cached content | 19.6 | -1.7
Firefox web browser | 10.5 | 1.7
Significant system energy saving without page load time increase
Applicable for other web browsers

## Slide 37: Evaluations on other environments and browser
Evaluation | Average system energy saving (%) | Average page load time increase (%)
Fast network (20 Mbps download, 10 Mbps upload, 50 ms RTT) | 21.8 | 0.1
3G network (3G network interface used) | 22.5 | 0.4
Web page loading with cached content | 19.6 | -1.7
Firefox web browser | 10.5 | 1.7
Significant system energy saving without page load time increase
Applicable for other web browsers
Speed Index metric increased only slightly (1.8%, on average)
(Above numbers are on Galaxy S5 Exynos big.LITTLE)

## Slide 38: Related work
Energy saving for mobile web browsers
  Chameleon [MobiSys11]: changes color to save energy on OLED screens
  Thagarajan et al. [WWW12]: measures energy and provides guidelines (e.g., avoid complex JavaScripts)
  Zhu et al. [HPCA13]: uses statistical inference models
    Limitations: Ignored JavaScript and dynamic contents

## Slide 39: Related work
Energy saving for mobile web browsers
  Chameleon [MobiSys11]: changes color to save energy on OLED screens
  Thagarajan et al. [WWW12]: measures energy and provides guidelines (e.g., avoid complex JavaScripts)
  Zhu et al. [HPCA13]: uses statistical inference models
    Limitations: Ignored JavaScript and dynamic contents
Our work
  Deal with trade-offs inside web browsers
    Others focus on the characteristics of web pages (primitives, colors, network accesses)
  Orthogonal with other approaches (e.g., changing color)
    Ours can be integrated with others to further improve energy efficiency
  Tested on real-world websites and smartphones

## Slide 40: Conclusion
Identify energy inefficiency issues in mobile web browsers
Propose energy saving techniques
  Network-aware Resource Processing
  Adaptive Content Painting
  Application-Assisted Scheduling
Implement on popular mobile web browsers (Chromium and Firefox for Android) on commercial smartphones (Samsung Galaxy S5 phones)
Evaluate on top 100 U.S. websites: save significant system energy while not increasing page load time
  24.4% system energy saving while decreasing 0.38% page load time on a big.LITTLE phone

## Slide 42: Case study: AAS technique
Significant increase of little cores utilization on big.LITTLE architecture
  E.g., 25% (Default) vs. 60% (Application-Assisted Scheduling)
Decrease of load on big cores
Chart: Time (sec)
Chart: Time (sec)
Default
Ours
Loading infusionsoft.com