## Slide 1: Performance Characterization & Call Reliability Diagnosis Support for Voice over LTE
Yunhan Jack Jia, Qi Alfred Chen, Z. Morley Mao, Jie Hui†, Kranthi Sontinei†, Alex Yoon†, Samson Kwong†, Kevin Lau†
University of Michigan, T-Mobile US Inc.†1
1 The views presented in this paper are as individuals and do not necessarily reflect any position of T-Mobile.

## Slide 2: Your voice call needs an upgrade
Illustration: Serge Bloch
Data network evolution:
  2G -> 3G -> 4G/LTE
Carrier’s voice call:
  All circuit-switched before 2014
Moving to a data-centric world
  Voice over LTE

## Slide 3: Voice over LTE
Deliver voice service as data flows within LTE network
Circuit-Switched Core
Packet-Switched Core
Telephony
Network
NodeB
ENodeB
Internet
For operators: reduce cost.
Performance benefit for users is unclear
1
Legacy call
VoLTE

## Slide 4: Challenge 1: Guarantee VoLTE performance
Guaranteeing QoS is challenging
High user expectation on VoLTE
  Goal: Replacing legacy call
Internet
Default Bearer
Dedicated Bearer
Gateway
User
2
Bit rat: 50 kbps,
Delay: 100 ms,

## Slide 5: Challenge 2: Diagnose VoLTE problems
VoLTE is a complex service
LTE Network
Multiple Layers
Multiple Layers
3G/2G Network
C\\\\\\\\\\\\
LTE Coverage Constraints
Existing approach: User tickets
  subjective, less accurate, coarse-grained
3
C\\\\\\\\\\\\
Cross-layer Interaction
C\\\\\\\\\\\\
Mobility Support
C\\\\\\\\\\\\
Device-network Interactions

## Slide 6: Problem statement
* Definition: Quality of Experience (QoE)
  Quality as seen by the end-user
  E.g., network call setup time vs. user perceived call setup time
Insufficient understanding of QoE of deployed VoLTE services
No effective support to capture and diagnose VoLTE problems
4

## Slide 7: Contributions
Systematic study of VoLTE in commercial deployment
  QoE quantification
  Empirical comparisons with legacy call & OTT VoIP
Diagnosis support for VoLTE reliability problems
  Devise tool to capture audio experience problems efficiently
    Covers three major symptoms in user tickets
  Uncover potential causes lying in the VoLTE protocols
    E.g., Up-to-50-second muting caused by mis-coordination between two different standards
5

## Slide 8: Outline
Performance characterization
  Methodology overview
  Result summary
Diagnosis support for VoLTE reliability problems
  Capturing audio experience problems
    Audio quality monitor
  Backend diagnosis engine
    Stress testing approach & diagnosis
    Case studies
Discussion
7

## Slide 9: Methodology overview
VoLTE service providers |  | 
OP-I | OP-II | OP-III
Comparing entities |  | 
Legacy call | Skype | Hangouts Voice
Metrics we study
  Smooth audio experience
    audio quality (MOS), mouth-to-ear delay and more
  Energy consumption
  Bandwidth requirement
  Reliability
    Call setup success rate
    Call drop rate
8

## Slide 10: Result overview
VoLTE delivers excellent audio quality with
  low bandwidth requirement
  less user-perceived call setup time
  low energy consumption
  won’t be affected by background traffic
Reliability still lags behind legacy call
  Higher call drop rate (5X)
  Higher call setup failure rate (8X)
9

## Slide 11: Call reliability support of VoLTE
VoLTE reliability support
  Circuit-switched fall back
  Single Radio Voice call Continuity
2G/3G Core
LTE Core
IMS
LTE
2G/3G
CSFB Procedure
SRVCC Procedure
However,
Challenge: Unsatisfying and varying network conditions
12
  VoLTE still fails to achieve a comparable reliability with legacy call
  Not all VoLTE problems are captured by traffic-analysis based approach

## Slide 12: Audio quality monitor overview
Use audio channel to detect QoE problems in real-time
Three types of VoLTE reliability problems
  Audio experience related problems
    Muting, garbled audio, intermittent audio, one-way audio
  Call setup failure
  Unintended call drop
Sampler
Context Collector
Audio
Quality
Monitor
Voice Call
15
Muting
Intermittent audio
Normal

## Slide 13: Audio quality monitor evaluation
  Implementation based on Android AudioRecord API
    Accuracy: FP: 0.65%, FN: 3.7%.
    Energy Overhead: +7% during VoLTE call
Complementary to traffic-based anomaly detection
  Closer to user experience, easier to deploy.
Useful diagnostic tool for operators
  Capture end-user audio problems objectively and accurately.
15
  More important: Understand the underlying causes of the problems

## Slide 14: Stress testing approach & diagnosis
Motivation
  Producing more problematic cases
  Gathering critical logs in lab settings
Lab settings
Automation
Device
Logging
Signal Strength
Network Events
Audio Quality Monitor
Anomaly Detection
Multi-Layer Logs
Network Logs
20
Cross-layer
Diagnosis
Potential
Causes

## Slide 15: Diagnose long audio muting problem
Problem capturing
  Up-to-50-second audio muting [Audio quality monitor]
  Triggered by signal strength degradation [Context collector]
Problem diagnosing
  Gap between radio link layer timeout and RTP layer timeout
Application
RTP
Control VoLTE call session
Transmit voice packet stream
RRC
RLC
Control the radio link connection
Transmit low level protocol data unit

## Slide 16: Lacking of coordination in cross-layer interactions
Application
Radio Link Disconnection
…
MaxRetx
Threshold
RTP
RRC
RLC
Reestablishment
Radio Link Failure
Timeout
Go to RRC_IDLE
RTP Timeout
Muting Start
Muting End
Radio Layer Timeout
=
RTT * maxRetxThreshold
+
RTP Timeout :
Recommended minimum value =
360/bandwidth(kbps)
Less than 5 seconds
30 to 50 seconds!
25
min{T301, T311}

## Slide 17: Lacking of coordination in cross-layer interactions
RTP layer makes wrong assumption on the radio layer failure recovery
  Cause: Gap between RTP (defined in RFC) and RRC/RLC (defined in 3GPP) protocol
  Also causing similar problems in Skype and Hangouts
Suggested solutions
    Reporting radio link events directly to application layer
Other case studies detailed in the paper
26

## Slide 18: Discussion
Limitation of diagnosis support
  Coverage
  Not fully automated
Follow-Up
  Integrating OEM support for QoE problem diagnosis
  Adding diagnosis support into protocols
27

## Slide 19: Summary
First systematic study of VoLTE QoE in the commercial deployment
Provide diagnosis support for VoLTE
  Audio quality monitor to capture problems
  Stress testing approach to collect essential information
  Cross-layer diagnosis support to understand problems
29

## Slide 20: Thank you!
Questions?