## Slide 1: Optimizing Smartphone Power Consumption through Dynamic Resolution Scaling
Songtao He1,2, Yunxin Liu1, Hucheng Zhou1
1Microsoft Research, Beijing, China
2University of Science and Technology of China, Hefei, China

## Slide 2: The “Arms Race” on display density
“Retina display”
Resolution: 720P (1280x720) -> 1080P (1920x1080) -> 2K (2560x1440)
806 PPI
3840x2160

## Slide 3: High display density -> high power cost
High system resource usage
  High GPU load
  More memory and more memory bandwidth
Significantly-reduced battery life
System power and GPU utilization in different display density (Galaxy S5 LTE-A)

## Slide 4: High display density -> compromised UX
Reduced frame rate
GFX benchmark frame rate in deferent display resolutions (Galaxy S5 LTE-A)
GPU frequency in running the Ridge Racer Slipstream game (Galaxy S5 LTE-A)
Overheating

## Slide 5: Solution: Dynamic Resolution Scaling (DRS)
Automatically adjust display resolution based user-screen distance
300 PPI

## Slide 6: Requirements and challenges
Change display resolution on the fly
  Real-time, per-frame
  No changes to apps and ROM
  Transparent from users
Measure user-screen distance
  Real-time
  Accurately
  Low power cost

## Slide 7: Background: Android graphics architecture

## Slide 8: Background: GPU graphics pipelines
Vertex processing
Pixel processing
Opportunity to reduce GPU workload via DRS

## Slide 9: Enable DRS through OpenGL-API interception
No modifications to apps and OS
  Work with legacy apps
  No ROM changes
Two interception layers
  Upper layer: adjusts display resolution
  Lower layer: handles composition

## Slide 10: Scale resolution down&up to reduce GPU workload
Upper layer
Lower layer
Ensure correctness: the same scaling factor must be used for the same frame in the two DRS layers

## Slide 11: Frame synchronization between DRS layers
Sync frame ID
Sync scaling factor
< 1ms
< 34 ms

## Slide 12: Ultrasonic based user-screen-distance detection
Real-time, accurate, and low-power
  40 KHz, ± 3mm, 5-6 mW
HC-SR04 ultrasonic sensors
MSP430 micro processor

## Slide 13: Determine the best display resolution
Maximize both user experience and power saving
Based on existing knowledge on human visual acuity

## Slide 14: Apply it to DRS
Decide the number of pixels from
  User-screen distance (D)
  Screen size (L)
  User visual acuity ()

## Slide 15: Evaluation
Samsung Galaxy S5 LTE-A smartphone
  2560x1440 pixels, 577 PPI, Adreno 420 GPU
  Samsung-customized ROM based on Android 4.4.2
30 GPU-intensive games
  Package size: 12 > 500 MB, 2 > 1,500 MB
  Our implementation supports all of them
Monsoon power monitor to measure system power
  14 games + 1 graphics benchmark (two scenes)

## Slide 16: Savings of Energy Per Frame (EPF)
On average 30.1% (up to 60.5%) EPF saving by halving the resolution
  2560x1440 -> 1280x720
  Assuming optimal vision
  29.4% average saving for the 14 games
More saving for normal vision

## Slide 17: User study
10 young students with at least normal vision
Play two games (Smash Hit and Temple Run Brave) for 10 minutes
  Randomly enable DRS for the first 5 minutes or the second 5 minutes
  Participants encouraged to change their postures and viewing distance freely
None of them could tell the existence of DRS
  Even with 136 times resolution changes for each participant in average
Live demo available during demo session, try it yourselves!

## Slide 18: Summary
Users suffer from extremely-high display density of smartphones
The first DRS system for smartphones
  Real-time, per-frame DRS
  Work on existing commercial smartphones and support legacy apps
  Automatic DRS with measured user-screen distance or manually configured
Ultrasonic based user-screen distance detection
  Real-time, accurate, low power, and cheap

## Slide 19
Thanks!
yunxin.liu@microsoft.com