## Slide 1
MagCode: NFC-Enabled Barcodes for
NFC-Disabled Smartphones
ACM MobiCom 2023
Donghui Dai, Zhenlin An, Qingrui Pan, Lei Yang
The Hong Kong Polytechnic University

## Slide 2: Background
Contactless Payment is Booming in Post-COVID World
Voice assistants are NOT always safe!
Barcode-based Payment
NFC-based Payment
Security!
User-friendly!
No alignment requirement!

## Slide 3: Motivation
NFC-unsupported Smartphone
NFC-supported Smartphone
Honor 8x Max
OPPO K9S
iPhone Series
Not All Cell Phones Support NFC Function
About 80% of the global population does not use NFC function in their cellphones today [1]
[1] “Worldwide NFC Technology Use Surges Over Last 24 Months,” 2022.

## Slide 4: Our Findings
Tap Cellphone Camera on the NFC Reader
NFC Principle: Magnetic Coupling
NFC Usage: Tap & Go
Cameras suffer from magnetic interference
generated by an NFC reader!

## Slide 5: Our Findings
The image shows alternant stripes when the camera is close to an NFC reader due to the magnetic interference

## Slide 6: Our Findings
Magnetic-inductive Barcode-like Strips on Captured Images
Frequency Increasing
Dense Strips Appear

## Slide 7: Why Alternant Strips?
The magnetic field imposes interference on the image line-by-line due to image sensor’s line-wise readout mechanism!
Read out line by line

## Slide 8: Proposed Communication
Achieving a simplex communication from an NFC reader to a camera, akin to scanning barcodes!

## Slide 9: Demo Video
https://donghui-dai.github.io/magcode/

## Slide 10
Challenge 1: How to distinguish phone models?
MagCode

## Slide 11
Response frequencies across 11 different phone models were tested. Their optimal response frequencies are as follows:
Challenge: Different phone models exhibit slightly different optimal magnetic-sensitive frequencies!
Challenge 1

## Slide 12
Our Solution
Use the frequency response as unclonable physical fingerprints to distinguish different phones
A simple KNN classifier achieves 95.6% average accuracy

## Slide 13
Challenge 2: How to modulate bits via magnetic interference?

## Slide 14
Challenge 2
The stripes are viewed as the result of under-sampling of the magnetic signal (500kHz readout vs 13.56MHz MI).

## Slide 15
Our Solution
Modulation Scheme:
On-off Keying Modulation
The presence or absence of MI represents bit one or bit zero
Bit 1: with MI signal
Bit 0: without MI signal
Bit 1: w/ MI-enabled strips
Bit 0: w/o MI-enabled strips

## Slide 16
Our Solution
Modulation Scheme: On-off Keying Modulation
Example: A magnetic interference-enabled data packet

## Slide 17
Challenge 3: How to ensure data integrity without ACK?
MagCode

## Slide 18: Fountain Codes
Data can be fully recovered with high probability given sufficient transmissions

## Slide 19
Implementation & Evaluation

## Slide 20: Implementation
Experiment Setting
A mobile app is developed for the smartphone to receive the NFC-enable magnetic data packet.

## Slide 21: Feasibility Results
MagCode system was successfully tested in 11 smartphones

## Slide 22: Safety Check
The average similarity score between two images across different metrics is 97.2%
MagCode does not damage the camera sensor

## Slide 23: Throughput
Even in a worse case P4, the communication throughput is 400 bps, which is sufficient to transmit an entire QR code V2 in less than 1s.

## Slide 24: Bit Error Rate
The BER increases as the increase of distance.
(BER < when distance < 20 mm )

## Slide 25: Impact of Transmit Power
MagCode (50 mW) is more energy-efficient than conventional NFC (100 mW)

## Slide 26: Impact of Distance
The BER increases as the increase of distance.
(BER < when distance < 20 mm )

## Slide 27
Conclusion
We first propose a novel cross-technology communication system between an NFC reader and the camera.
We demonstrate the feasibility and safety of such communication across mainstream smartphone models.
We design and implement a stack of protocols to achieve such a simplex communication.

## Slide 28: Thank You!
https://donghui-dai.github.io/magcode/