## Slide 1: Fine-Grained RFID Localization with a Handheld Device via Complex Controlled Polarization
Laura Dodds, Isaac Perper, Aline Eid, Fadel Adib
Cartesian
Systems

## Slide 2: Fine-Grained RFID Localization has many applications
Retail
Warehouses
Manufacturing

## Slide 3: State-of-the-Art Localization
Infrastructure-Based
[MobiCom’17, SIGCOMM’13, SIGCOMM’15, …]

## Slide 4: State-of-the-Art Localization
Robot-Based
[MobiCom’13, SenSys’21, RSS’22, …]
Expensive ($10s of k / robot)
Difficult to Scale (e.g., stairs)
Very Expensive ($100k/store)
Infrastructure-Based
[MobiCom’17, SIGCOMM’13, SIGCOMM’15, …]

## Slide 5
The majority of RFID adoption uses handheld readers

## Slide 6
The majority of RFID adoption uses handheld readers
No Accurate Localization
Affordable (~$1,000)

## Slide 7: POLAR
First fine-grained, handheld RFID localization system
Introduce techniques for complex-controlled polarization and joint tag discovery and localization
Achieves a median and 90th percentile of 9cm and 17cm, respectively

## Slide 8: Problem: Existing handheld readers cannot localize tags across orientations

## Slide 9: Localizing across orientation is challenging due to polarization
Existing portable readers use circularly polarized antennas

## Slide 10: Localizing across orientation is challenging due to polarization
Existing portable readers use circularly polarized antennas
Circular polarization can read tags across orientation

## Slide 11: Localizing across orientation is challenging due to polarization
Existing portable readers use circularly polarized antennas
Circular polarization can read tags across orientation
…but they cannot perform accurate phase-based localization [ISPN ‘18, MobiCom ‘16, RFID-TA ’22]

## Slide 12: Solution: Introduce Complex-Controlled Polarization to Power and Localize across Orientation
Linearly Polarized Antenna
Recall: Circularly Polarized

## Slide 13: Solution: Introduce Complex-Controlled Polarization to Power and Localize across Orientation
C1
C2
Complex
Numbers
(Shift by 90°)
Linearly Polarized Antenna

## Slide 14: Solution: Introduce Complex-Controlled Polarization to Power and Localize across Orientation
C1
C2
Complex
Numbers

## Slide 15
Complex-controlled polarization also enables generating arbitrary linear polarization
1
0

## Slide 16
Complex-controlled polarization also enables generating arbitrary linear polarization
1
0
Vertical polarization
0
1
Horizontal polarization
cos(30°)
sin(30°)
30° polarization
Linearly polarized signals measure consistent phases and enable accurate phase-based localization

## Slide 17: Complex-controlled polarization enables generating both circularly polarized and linearly polarized signals
Powers tags across orientations
Localizes tags across orientations

## Slide 18: Complex-controlled polarization enables generating both circularly polarized and linearly polarized signals

## Slide 19: Complex-controlled polarization enables generating both circularly polarized and linearly polarized signals
But how can we combine circular & linear polarization to efficiently power & localize tags?

## Slide 20: Solution: Joint Tag Discovery and Localization (JTDL) Enables Zero-Overhead Localization

## Slide 21: Solution: Joint Tag Discovery and Localization (JTDL) Enables Zero-Overhead Localization
fpower
fpower
flocalize
flocalize
POLAR can jointly power & localize across orientations
Estimates phase by multiplexing linear transmissions & performing polarization projection at the receiver
(details in the paper)

## Slide 22: Implementation
BladeRF software defined radios to apply complex-control polarization
Raspberry Pi
EPC Gen 2 Protocol
Intel RealSense camera for self-tracking
Custom-designed bowtie antenna
Smarttrac RFID Tags
Software
Defined
Radios
Antennas
RFID Tag
Intel RealSense Camera
System can be built for <$1000

## Slide 23: 3D Localization Accuracy
Place >25 tags at angles from 0° to 360°
Over 75 location measurements in total
Moved device around the environment
1.28m
88cm
17cm
9cm
POLAR achieves fine-grained (sub-10cm) localization accuracy across orientations significantly outperforming a circularly polarized baseline

## Slide 24: Read Rate vs Distance
Place >30 tags at angles from 0° to 360°
Moved device around a single plane
Varied the distance between tag plane and device plane
Measured read rate: % of tags that the device could read
POLAR can read tags across orientations and distances significantly outperforming a linearly polarized baseline

## Slide 25: Conclusion
First fine-grained, handheld RFID localization system
Complex-controlled polarization and Joint Tag Discovery and Localization to overcome tag orientation
Achieves fine-grained localization (9cm)
  10x improvement in accuracy over past handheld-based RFID systems