## Slide 1: GPSMirror: Expanding Accurate GPS Positioning to Shadowed and Indoor Regions with Backscatter
Huixin Dong1, Yirong Xie1, Xianan Zhang1, Wei Wang1*,
Xinyu Zhang2 and Jianhua He3
1School of Electronic Information
and Communication
2Electrical and Computer
Engineering
3School of Computer Science
and electrical Engineering

## Slide 2: GPS services fail in shadowed region
[1] K.Chen and G.Tan. 2018. BikeGPS: Accurate Localization of Shared Bikes in Street Canyons via Low-Level GPS Cooperation. MobiSys ’18.
[2] S.Nirjon, J.Liu, G.DeJean, B.Priyantha, Y.Jin and T.Hart. 2014. COIN-GPS: indoor localization from direct GPS receiving. MobiSys’14.
Urban Canyon
Flyover Shadow
Gas/Dust Factory
Conventional GPS provides localization with high error (hundreds of meters[1]) or even cannot localization[2] in these shadowed regions.

## Slide 3: GPS relays are hard to deploy
Receive antenna fixed in open area.
Plug-in
power supply
Long cable
Transmit Antenna
High Deployment Cost
Cannot Deploy
Hard to Deploy
Block
The shadowed region.
Not Available

## Slide 4: Our Idea: Ultra-low-power backscattering
Backscatter Tag
Backscatter Tag
Backscatter Tag
Design a uW-level backscatter tag that provides comparable coverage to commercial relays.

## Slide 5: New positioning opportunities of backscattering GPS
Common delay error
The relayed GPS signals cannot collaborate with non-relayed GPS signals since they contain different propagation delay.
Uncertain delay
Real
distance
Delay match to the real distance
The scattered and non-scattered GPS signals can collaborate to provide better positioning service.

## Slide 6: Requirements on scattering the GPS signals
uW-level power consumption for easy deployment.
Power
Comparable coverage to commercial GPS relays.
Gain
Sensitive to scatter weak GPS signals (-125dBm).
Sensitivity
Flat gain over GPS L1 band.
Bandwidth

## Slide 7: Existing backscatter devices
RF switch-based backscatters
WISP Platform
TIE’08
RF-Transformer
MobiCom’22
Ambient Backscatter
SIGCOMM’13
FS Backscatter
SIGCOMM 2016
Power
Gain
Existing tunnel diode-based backscatters
Tunnel Scatter MobiCom’19
Tunnel Emitter MobiCom’20
Power
Gain
Sensitivity
Bandwidth
Can we design a backscatter system to meet all the requirements?

## Slide 8: Challenge: Bandwidth
Design 1: Matching Parasitic Parameters.
Equivalent Circuit
r
Negative Resistance
Parasitic Parameters
Tunnel Diode
Design 2: High-precision impedance control.
Circuit Board.
Rogers RO4035B (0.508)
GND
Strip Line
Aluminum
GND
Tune
Aluminum
Copper (0.035)
Copper (0.035)
Unit: mm
Tunable structure for precisely resonance control
Equal to a small adjustable capacitor
r
Resonator 1
Resonator 2

## Slide 9: Challenge: Sensitivity
Tunnel Emitter MobiCom’20
Our insight:
Minimizing the circuit loss, noise and maximize the signal reception.
-90 dBm ~ -100 dBm
Reported threshold for injection-locked amplify of the SOTA tunnel diode-based backscatter:
Signal Reception
Return Loss
Current noise
Signal Out
DC Bias
Tunnel Diode
Screw
Signal In
Tunnel diode amplifier
~ -125 dBm
GPS signals at the ground

## Slide 10: Challenge: Sensitivity
Design 1:
Reduce the return loss caused by components solder.
Signal In
Signal Out
No reflection
Solder
Capacitor
Impedance change
Return Loss
Signal In
Signal out
Lower the return loss by about 15 dB
Amplitude
Control
Phase Control

## Slide 11: Challenge: Sensitivity
Voltage (mV)
Current (mA)
Minimum noise point
IV-Curve of selected diodes
Design 2: Search the minimum noise operation point
Customize radiation pattern for better reception
Helix
Antenna
Design 3: Customized radiation pattern for better reception

## Slide 12: Localization under inadequate satellites
C/N0 measurements of
non-scattered GPS signals
C/N0 measurements of
scattered GPS signals
Separate distance raw measurements (PrM，AdrM) with the same index.
XPRN-5: PrM1，AdrM1
XPRN-20: PrM2，AdrM2
XPRN-5’: PrM1’，AdrM1 ’
XPRN-20’: PrM2’，AdrM2 ’
Duplex the measurements for GPS localization under inadequate satellites.
From
Virtual Satellites
A piece of “Carrier to Noise Density Ratio (C/N0 ) ” raw measurements of scattered and non-scattered GPS signals

## Slide 13: Differential positioning for accuracy improvement
Capable to eliminate the common delay error in distance measurements of GPS signals.
Common delay error
ΔX1=X1’-X1
ΔX2=X2’-X2
···
ΔXn=Xn’-Xn
Eliminate Common Error by differential
Modelling the vector b from a GPSMirror tag to smartphone
b
Differential positioning

## Slide 14: Implementation and hardware performance
GPSMirror Tag
-125dBm Sensitivity with variance less than 1.3dB.
0-30dB adjustable gain.
Compatible with smartphones.
～126uW power consumption

## Slide 15: Coverage performance
Urban Canyon
Flat Room
27.7 m away from the tag with about 4 dB gain in C/N0
A 20m14m room can be covered by a single GPSMirror tag with > 3dB gain in C/N0

## Slide 16: Localization accuracy
Static Localization Error
3.7 m
4.6 m
Dynamic Localization Error Indoor
4.5 m

## Slide 17: Summary
The first backscatter system that scatters signals from orbiting satellites. The hardware design pushes the limit of backscatter that it can re-radiate weak GPS signals as low as -125 dBm with over 20 dB flat gain.
We propose novel GPS positioning algorithms based on GPSMirror tags to extend GPS positioning services in shadowed or indoor regions. It works seamlessly with off-the-shelf smartphones without any hardware or firmware modification.
We implement and evaluate the GPSMirror in real world environments using off-the-shelf smartphones from different manufacturers. Our experiments verify the feasibility and compatibility of GPSMirror .

## Slide 18
Thanks!
Q&A