## Slide 1
MUSE-Fi: Contactless MUti-person SEnsing Exploiting Near-field
Wi-Fi Channel Variation
Jingzhi Hu*, Tianyue Zheng*, Zhe Chen, Hongbo Wang, Jun Luo
Nanyang Technological University (Singapore) and Fudan University (China)
Presented by Yinghui He, Zhejiang University (China)

## Slide 2
CONTENTS
01 Background on Wi-Fi Sensing
02 Principle of Near-field Sensing
03 Insights into Multi-person Sensing
04 Shaping up MUSE-Fi
05 Experimental Results

## Slide 3
Background on Wi-Fi Sensing
Wi-Fi human sensing basics
  Channel state information (CSI) obtained from the long training sequence (LTS) in data frames
  Sensing with variations of CSI caused by human movements
Various important applications
  Vital signs monitoring, gesture detection, activity recognition
  Localization and motion tracking
Multi-person sensing faces challenges
  Inadequate bandwidth and antennas insufficient spatial resolution
20~160MHz bandwidth
Basics

## Slide 4
Background on Wi-Fi Sensing
Now and Then
Existing solutions
  GHz-level bandwidth to improve range resolution
  Many (distributed) antennas for higher spatial resolution
  Signal processing techniques for post-processing
  Drawbacks: extra spectrum resources; hard for ubiquitous deployment; complex controlling protocols; unguaranteed & insufficient separability
Our way: exploiting natural communications setting
  Scene: User equipment (UE) in the near-field () of a user
  Idea: CSI variations of each UE-AP link caused by its near-field user dominate interference from others
  Meaning: Naturally extend Wi-Fi comm. to support multi-person sensing
  Potential Applications: VR/AR/MR/XR
    Reduce peripheral sensors of headsets
    Provide contextual and localizational information near Wi-Fi devices

## Slide 5
Background on Wi-Fi Sensing
Challenge and Solution
Challenges
  Idea of near-field sensing lacks of theoretical analysis, experimental verification, and protocol integration
  Realistic data traffic in Wi-Fi, especially in multi-UE scenarios, is of unsaturated, even low frequency, causing sparsity in CSI samples.
Solution: MUSE-Fi (MUlti-person SEnsing system leveraging Wi-Fi)
  Theoretical characterization, prototyping, and experiment evaluations
  Various WiFi-compatible sensing strategies
  Recovery algorithm to tackle sparsity in CSI sampling rate
Frame arrival rates when one or two users stream 1080p videos

## Slide 6
Principle of Near-field Sensing (NFS)
More on Wi-Fi sensing basics
Near-field domination effect (NFDE)
  As CSI variations mater, Power of CSI variation , : intensity/speed of movement
  As of near-field subject is much smaller than of interferers, variation power of subject dominates of interferer (near-field domination)
Derivation of feasible regions for NFS
  Metric: variation to interference ratio (VIR)
  Illustration and observation:
    constitutes Cassini ovals, physically guarantee boundaries for user separation
    Subject and interferer can be very close (0.3-0.5m)
Channel between AP and UE = Reflection channel via subject S + static channel + env. dynamic channel
Path loss exponent
Distance S to UE
Distance AP to S
Envir. dynamic channel gain as an interference
=50

## Slide 7
Insights of Multi-person Sensing (MPS)
Ideal multi-person () scenes
  Symmetry cases and normalized parameters
  (a) Radial symmetry case for maximum
  (b) Mirror symmetry case for minimum
Proof of concept experiments
  Respirations of closely-sit persons (even by-shoulder) can be well separated
  NFS works for different motion intensities: stronger signals do not mess up weaker ones
=50
peaks at 51 around AP-UE distance 3m
remains 0.34m for

## Slide 8
Shaping up MUSE-Fi
Components, Strategies, Compatibility
Hardware Components
  A commodity AP and multiple UEs carried by individual users:
    All devices follow prevalent Wi-Fi 5/6 standard
    CSI can be obtained from the received frames
    No additional antennas or bandwidth expansion
Strategies compatible with WiFi-ISAC (integrated sensing & communication)
  Uplink (UL)-CSI: AP obtains CSI from UEs' UL traffic
    Centralized sensing at AP, covering all users
  Downlink (DL)-CSI: UEs obtain CSI from AP's DL traffic
    Distributed sensing at UE, privacy preserving
  UL-BFI: Beamforming feedback info (BFI) in UEs' UL traffic
    As BFI is sent out in plain-text, sensing can be carried out at any Wi-Fi devices capable of hearing the traffic (WiKI-Eve in CCS’23)

## Slide 9
Shaping up MUSE-Fi
Sparse Recovery Algorithm (SRA)
Goal: handle CSI sample sparsity in realistic data traffic
Data processing pipeline
  Divide sparse and non-sparse time slices
  Linearly resample/temporarily fill
  Transform resampled CSI time series into spectrogram featuring freq. components
  Normalize spectrogram and re-assign `no-data` labels to sparse slices
Sparse slice recovery with TCN-AE
  Adopts temporal conv. network (TCN) due to its parameter efficiency
  TCN is featured by dilated conv.
Self-supervised training
  Use non-sparse slices as labeled training data for sparse slices
output
input
kernel
: dilation factor

## Slide 10
Experiment Results
Implementation and Evaluations
Implementation
  AP: commercial Netgear router
  UE: iPhone 13, iPhone X, OnePlus 10T, Acer TravelMate laptops
  Retrieval of CSI: with the help of PicoScenes or Nexmon hardware
  Retrieval of BFI: from Action No ACK frames captured by Wireshark software
  Data traffic: e.g., video streaming
Evaluating SRA
  Low MSE losses of the recovery in case of resp., gesture, and activity sensing (<10-2)
Respiration Monitoring
  MUSE-Fi recovers a clear respiration signal
  NFS halves the average spectral entropy
  Baseline: non-near-field sensing setup for multi-person sensing

## Slide 11
Experiment Results
Evaluation Continued
Gesture detection
  Gestures: circle (CR), front-back (FB), slide (SL), star (ST), wave (WV), and zig-zag (ZZ)
  Result: MUSE-Fi achieves about 98% accuracy for arbitrary subject thanks to near-field domination, while non-near-field baseline 57%
Activity recognition
  Actions: bending (BD), jumping (JM), rotating (RT), sitting down (SD), standing up (SU), and walking (WL).
  Result: MUSE-Fi 98% vs. non-near-field baseline 52%
Extended experiments
  UE is kept in subject's pocket: NLoS with AP
  Similar accuracy is achieved

## Slide 12
Q & A