## Slide 1: UniScatter: a Metamaterial Backscatter Tag for Wideband Joint Communication and Radar Sensing
Kun Qian, Lulu Yao, Kai Zheng, Xinyu Zhang, Tse Nga Ng
Presenter: John Nolan
University of California San Diego

## Slide 2: Joint Communication and Sensing (JCAS)
Comm Link
Target Echo
JCAS brings new opportunities for future wireless communication and sensing.
High spectrum efficiency due to shared spectrum
Cost saving due to shared hardware
The feasibility of JCAS is due to the similar signal processing flows of sensing and communication.

## Slide 3: Enabling JCAS for Passive Internet of Things
Comm Link
Target Echo
For the Internet of Things, some passive objects need to be simultaneously localized and communicated with.
The JCAS for passive IoT can be achieved with backscatter technologies.

## Slide 4: Applications of Passive IoT with JCAS
Warehouse management
Intelligent transportation infrastructure
Whole-home HOI
Advertising

## Slide 5: Emerging Challenges for Passive IoT
Massive connection
Communication with >10 objects per .
High-resolution sensing
Localization with sub-meter accuracy
Warehouse management
Intelligent transportation infrastructure

## Slide 6: From Microwave Band to Mmwave Band
Designing backscatter tags working at mmWave band
Microwave bandwidth is usually at MHz level (e.g., 100MHz@2.4GHz).
MmWave bandwidth usually achieves GHz-level (e.g., 14GHz@60GHz).
Key solution to solve both challenges: wider bandwidth
Communication: wider bandwidth  larger capacity  More connections
Sensing: wider bandwidth  Higher resolution

## Slide 7: Design Challenges of MmWave Backscatter
Challenge #1: heterogeneous readers in the ultrawide mmWave band
MmWave tags need to work through ultrawide bandwidth.
24 GHz Radar
79 GHz Radar
5G@28 GHz
WiGig@60 GHz

## Slide 8: Design Challenges of MmWave Backscatter
Challenge #2: power loss due to smaller tag size
MmWave tags must have scalable sizes.
900 MHz
24 GHz
28 GHz
60 GHz
79 GHz
12 m
2.3 m
Frequency
Range
2.2 m
1.5 m
1.3 m

## Slide 9: MmWave Backscatter Tag Structure
Retroreflector for maximum power efficiency
Specular reflection
7
Diffusion
Reader
Retroreflection
7
Modulator for seamless data modulation
0110010…
Requirements
Scalable size
Ultrawide bandwidth
Tag
Modulator

## Slide 10: Our Solution
Designing ultrawide-band and scalable tags using metamaterials
Graphene modulator
3D printed retroreflector
UniScatter

## Slide 11: UniScatter Design
Modulator design
Graphene with ultra-wideband tunable reflection power.
Metal coating patterns increase scalability without sacrificing tuning rate.
Graphene
Electrolyte
Graphene
Support
Ground
+
-
Electrode
modulator
Modulator structure
Metal coating
Tuning rate <10 Hz
Tuning rate >100 Hz
Power level #1
Power level #2
Electrode
Gap

## Slide 12: UniScatter Design
Retroreflector design
Luneburg lens has both ultrawide bandwidth and scalable size.
Sub problems #1: aligning the spherical lens with the flat modulator
Computational optics reshapes the lens while retaining the retroreflectivity.
Sub problems #2: fabricating the lens with non-uniform material properties
Discretizing the lens into small cubes
Controlling the filling ratio of uniform material in each cube
Rod
Tunable part

## Slide 13: Tag Detection and Decoding
Coding Peaks
Radar profile
Doppler spectrum
We adopt frequency shift keying to encode tag bits.
Tag coding can be reliably detected in the Doppler frequency spectrum.
Tag bits can be successively decoded while the co-located object is being tracked.
Workflow

## Slide 14: Implementation
5 cm
1 cm
Graphene modulator
3D printed retroreflector
3D printed support
Power management circuit
9.4 cm
5 cm
Charging
Discharging

## Slide 15: Field Experiments: Intelligent Transportation Infrastructure
Transportation infrastructure responds to radars on vehicles by reflecting radar signals.
Road signs, traffic lights, etc.
Radar
Power
management
Modulation
Controller
Tag

## Slide 16: Evaluation of Tag Coverage
Tag-Radar Distance
Tag-Radar angle
Radar frequency
UniScatter achieves a wide coverage in both space and frequency.
Distance
Azimuth/Elevation
Bandwidth

## Slide 17: Conclusion
We have designed UniScatter, a metamaterial-based tag for mmWave joint sensing and communication.
A novel modulator + retroreflector tag architecture for the mmWave band
Ultrawide-band and scalable modulator and retroreflector design
We have fabricated and validated UniScatter.
Novel fabrication processes for high-frequency RF components
Wide coverage across both space and frequency

## Slide 18: Thank you!
Any Questions?