## Slide 1: Scattering from Rough Surfaces in 100+ GHz Wireless Mobile Networks: From Theory to Experiments
Ruiyi Shen and Yasaman Ghasempour
Department of Electrical and Computer Engineering, Princeton University
ACM MobiCom 2023, Madrid, Spain

## Slide 2
Wireless Links at 100+ GHz Frequencies
ACM MobiCom 2023, Madrid, Spain

## Slide 3
Wireless Links at 100+ GHz Frequencies
Increasingly directional beams at 100+ GHz frequencies
ACM MobiCom 2023, Madrid, Spain

## Slide 4
Wireless Links at 100+ GHz Frequencies
Increasingly directional beams at 100+ GHz frequencies
Lower chance for establishing LOS link
ACM MobiCom 2023, Madrid, Spain

## Slide 5
Wireless Links at 100+ GHz Frequencies
Increasingly directional beams at 100+ GHz frequencies
Lower chance for establishing LOS link
NLOS links become crucial
Surface reflection behavior has been oversimplified
ACM MobiCom 2023, Madrid, Spain

## Slide 6
Reflection at High Frequencies
At lower frequencies, most surfaces are considered smooth
They can be electromagnetically rough at sub-THz frequencies
3
Why is understanding rough scattering important?
ACM MobiCom 2023, Madrid, Spain
Indoor
Outdoor

## Slide 7
Half-Power Scattering Width (HPSW)
Impact on Peak Specular Power and Angular Coverage
Smooth surfaces: large specular SNR, but drops rapidly at non-specular angles
Rough surfaces: lower specular SNR, but comparable SNR at non-specular angles
Smooth Surface
Rough Surface
4
Low HPSW
High HPSW
ACM MobiCom 2023, Madrid, Spain
Angle
Power
Angle
Power

## Slide 8
Impact on DL/UL Channel Reciprocity
Incident angle dependency of scattering results in non-reciprocal DL/UL channels
Adds overhead to beam search procedure
Downlink
Uplink
5
ACM MobiCom 2023, Madrid, Spain

## Slide 9
Defining Surface Roughness
The vertical roughness of a surface is defined with
  RMS height ()
6
ACM MobiCom 2023, Madrid, Spain

## Slide 10
Defining Surface Roughness
6
Surface roughness can be classified with Rayleigh’s Criterion
The vertical roughness of a surface is defined with
  RMS height ()
140 GHz: 300 – 500
ACM MobiCom 2023, Madrid, Spain

## Slide 11
Scattering Power at the Specular Angle
where
7
has an inverse exponential relationship with and frequency
ACM MobiCom 2023, Madrid, Spain

## Slide 12
Scattering Power at Non-specular Angles
No simple closed form equation to solve for
The Integral Equation Model (IEM) provides a bistatic scattering coefficient
8
ACM MobiCom 2023, Madrid, Spain

## Slide 13
Scattering Power at Non-specular Angles
No simple closed form equation to solve for
The Integral Equation Model (IEM) provides a bistatic scattering coefficient
8
ACM MobiCom 2023, Madrid, Spain

## Slide 14
Can we measure surface roughness?
9
Putting surface samples under the microscope
Can we calculate rough scattering pattern?
Solving Maxwell’s Equations
ACM MobiCom 2023, Madrid, Spain
More scalable solutions?

## Slide 15
10
Categorizing the roughness level of surfaces is sufficient!
Smooth
Semi-Rough
Rough
ACM MobiCom 2023, Madrid, Spain

## Slide 16
11
Objective: Categorize Roughness Level at Minimal Overhead
Single reflection provides insufficient information on rough scattering
Frequency Spectrum?
ACM MobiCom 2023, Madrid, Spain

## Slide 17
Inferring Roughness via Angular Diversity
Beam n-2
Beam n+2
…
…
……
……
FFT
Inter-Beam Spectral Correlation
Smooth
Semi-Rough
Rough
11
Beam n:
ACM MobiCom 2023, Madrid, Spain

## Slide 18
Does not require specific motion pattern from TX/RX
Inferring Roughness via Angular Diversity
11
Adds minimal overhead on top of conventional beam search protocol
ACM MobiCom 2023, Madrid, Spain
…
…

## Slide 19
Experimental Setup
12
ACM MobiCom 2023, Madrid, Spain

## Slide 20
Surface Samples Tested
Sample | (mm) | Classification
Metal Sheet | 0.01 | Smooth
3D Printed Metal #1 | 0.28 | Semi-Rough
3D Printed Metal #2 | 0.66 | Very Rough
Tiles #1-3 | 0.05-0.08 | Smooth
Bricks #1-3 | 0.22-0.32 | Semi-Rough
Redstones #1-3 | 0.23-0.39 | Semi-Rough
Granite #1-3 | 0.61-0.90 | Very Rough
Sample |  | Classification
Metal Sheet | 0.01 | Smooth
3D Printed Metal #1 | 0.28 | Semi-Rough
3D Printed Metal #2 | 0.66 | Very Rough
Tiles #1-3 | 0.05-0.08 | Smooth
Bricks #1-3 | 0.22-0.32 | Semi-Rough
Redstones #1-3 | 0.23-0.39 | Semi-Rough
Granite #1-3 | 0.61-0.90 | Very Rough
13
ACM MobiCom 2023, Madrid, Spain

## Slide 21
Evaluating Peak Specular SNR
SNR at specular angle exponentially decreases as a function of RMS height
14
ACM MobiCom 2023, Madrid, Spain
0
0.2
0.4
0.6
0.8
1
RMS Height (mm)
-20
-15
-10
-5
0
5
10
15
N
o
r
m
a
l
i
z
e
d
S
N
R
(
d
B
)
Non-metal samples
Metal sample
Model

## Slide 22
Evaluating Scattering Width
15
TX
RX
ACM MobiCom 2023, Madrid, Spain

## Slide 23
Increasing roughness
> 15°
Rough
Semi-Rough
Smooth
Evaluating Scattering Width
Scattering from rough surfaces has weaker specular power, but wider scattering profile
15
-5
0
5
Angular Deviation (deg)
-20
-15
-10
-5
0
N
o
r
m
a
l
i
z
e
d
S
N
R
(
d
B
)
Tile (h
rms
= 0.083 mm)
Brick (h
rms
= 0.246 mm)
Redstone (h
rms
= 0.377 mm)
Granite (h
rms
= 0.748 mm)
Increasing
roughness
ACM MobiCom 2023, Madrid, Spain
deg

## Slide 24
35
40
45
50
55
Scattering Angle (
s
)
0
1
2
3
4
5
P
o
w
e
r
D
i
f
f
e
r
e
n
c
e
(
d
B
)
Tile
Brick
Redstone
Granite
Evaluating Non-Reciprocal DL/UL Channels
Rough surface scattering creates evident power difference between DL and UL channels
16
Increasing deviation from specular angle
Increasing roughness
TX
RX
ACM MobiCom 2023, Madrid, Spain

## Slide 25
Spectral-Spatial Correlation for Different Surfaces
Correlation between specular and non-specular spectra identifies surface roughness
17
ACM MobiCom 2023, Madrid, Spain
deg

## Slide 26
Conclusion and Future Work
A comprehensive theoretical and experimental analysis on the impact of rough scattering on sub-THz wireless networks
A low-overhead roughness characterization method to categorize surfaces
For ongoing work, we go beyond classification to numerically estimate surface parameters
18
ACM MobiCom 2023, Madrid, Spain

## Slide 27
Thank you!
ACM MobiCom 2023, Madrid, Spain