## Slide 1
Ne(RF)2: Neural Radio-Frequency Radiance Fields
Xiaopeng Zhao, Zhenlin An, Qingrui Pan, Lei Yang
The Hong Kong Polytechnic University

## Slide 2
Precisely modeling the propagation of RF signals remains a long-standing problem
Complicated interactions between the RF signal and the obstacles

## Slide 3
Optical NeRF:
Synthesize images from arbitrary view directions
B.Mildenhall etc., “NeRF: Representing Scenes as Neural Radiance Fields for View Synthesis,” in ECCV 2020.

## Slide 4
Task Comparability
Pixel Array RF Ant. Array & Images Spatial Spectra
The task similarity inspired our NeRF2
Optical Pixel Array
RF Antenna Array
VS

## Slide 5
Problem: How to predict the received RF signals when TX/RX is located at an arbitrary position?
NeRF2 represents a scene as a neural radiance field, which is trained by a small number of signal measurements
Predict received signal
when TX is here
RX

## Slide 6
Background: Spatial Spectrum as Optical Image
Spatial spectrum shows the power of RF signals originating from all directions
Task: synthesize the spatial spectrum given the position of a TX/RX

## Slide 7
Demo Video
https://xpengzhao.github.io/NeRF2/

## Slide 8
RX
Discretize the scene into a finite number of 3D voxels
A direction
A direction is a path across a line of voxels
The scene is discretized into 3D voxels
NeRF2 Design

## Slide 9
RX
Direct Incident
Reflection
Diffraction
The Huygens–Fresnel principle suggests that a voxel can be considered as a new radiance source
Radiance
Attenuation
Voxels on a directional path become new radiation sources:
Emitting signals to RX along that direction
NeRF2 Design

## Slide 10
RX
MLP
Radiance
Attenuation
（Pvoxel, , PTX）
Similar to NeRF, two MLPs are trained to model the physical and radiative characteristics of each voxel
Details refer to our paper
NeRF2 Design

## Slide 11
RX
Taking ray tracing to know the RF signal from this direction
Predict the received signal at the direction
Integral along the direction
The result of ray tracing is an accumulation of radiations of voxels on the direction
NeRF2 Design

## Slide 12
RX
NeRF2 Design
A spatial spectrum is a result of ray tracing across all potential directions
Integral along all directions
Predict the received signal at all directions

## Slide 13
What is NeRF2 used for?
Indoor Localization
5G FDD MIMO

## Slide 14
Case 1: Augmented Localization by NeRF2
Synthesizing samples at arbitrary locations by NeRF2
Deep learning-based AoA estimation algorithm requires a large number of samples

## Slide 15
NeRF2 can synthesize more training samples
collect 1000 training samples
Use 1000 samples to train NeRF2
Use NeRF2 to generate extra 9000 samples
Train a DNN localization model with (1000 + 9000) samples
The quality of the synthetic dataset generated by NeRF2 is as good as the true dataset

## Slide 16
NeRF2 can synthesize more training samples
Notes: 10‘

## Slide 17
Case 2: Channel Estimation/Prediction
Uplink Channel in frequency 1
Downlink Channel in frequency 2
How to estimate the downlink channel using the uplink parameters?
5G FDD base stations employ two different frequencies for the uplink and downlink
1. Report presence
2. Pilot tone
3. Send back the CSI

## Slide 18
RX
Using the uplink as a location indictor (location) to predict the downlink beamforming parameters
MLP
Radiance
Attenuation
（Pvoxel, , Uplink CSl ）
Use NeRF2 to help FDD channel prediction

## Slide 19
Use NeRF2 to help FDD channel prediction
NeRF2 is 5.97 dB better SNR than the STOA work
2

## Slide 20
Conclusion
We translate the neural radiance field to the RF domain.
We propose the NeRF2-enabled turbo-learning.
We conduct real-life field studies in terms of RFID, BLE, and 5G systems.
Our code is available here!
Notes: 12‘